## Slide 1
Google 7/11 2013
Drinking from the Firehose
The Belt machine model
in the Mill™ CPU Architecture

## Slide 2
addsx(b2, b5)
The Mill Architecture
The Belt -
A new machine model
New to the Mill:
No general registers or rename registers
fast, small, low-power bypass
No issue, dispatch, or retire stages
short pipe, low mispredict penalty
No encoded result addresses
compact code
Multi-result operations and calls
regular ISA for simpler compiler

## Slide 3: Two architectures
cores: 1 core
issuing: 8 operations
clock rate: 456 MHz
power: 1.1 Watts
performance: 3.6 Gips
price: $17 dollars
cores: 4 cores
issuing: 4 operations
clock rate: 3300 MHz
power: 130 Watts
performance: 52.8 Gips
price: $885 dollars
in-order VLIW DSP
out-of-order superscalar
406 Mips/W
59 Mips/$
3272 Mips/W
211 Mips/$

## Slide 4: Two architectures
out-of-order superscalar
406 Mips/W
59 Mips/$
in-order VLIW DSP
3272 Mips/W
211 Mips/$
Comparison per core
Superscalar gives:
3.6x better performance
but costs:
30x more power
13x more money

## Slide 5: Which is better?
DSP efficiency
- on general-purpose workloads
Why huge cost in both power and price?
32 vs. 64 bit
3,600 mips vs. 52,800 mips
incompatible workloads
signal processing ≠ general-purpose
goal – and technical challenge:

## Slide 6
Our result:
cores: 2 cores
issuing: 33 operations
clock rate: 1200 MHz
power: 28 Watts
performance: 79.3 Gips
price: $225 dollars
OOTBC Mill Gold.x2
2832 Mips/W
352 Mips/$
Clock, power: our best estimate after several years in sim
Price: wild guess

## Slide 7
Our result
vs. OOO superscalar:
vs. VLIW DSP:
11x more performance
12x more power
6.5x more money
OOTBC Mill Gold.x2
2832 Mips/W
352 Mips/$
Comparison per core
2.3x more performance
2.3x less power
1.9x less money

## Slide 8
Our result:
cores: 2 cores
issuing: 33 operations
clock rate: 1200 MHz
power: 28 Watts
performance: 79.3 Gips
price: $225 dollars
OOTBC Mill Gold.x2
2832 Mips/W
352 Mips/$

## Slide 9
Caution!
33 independent MIMD operations
NOT counting each SIMD vector element!
(if counting elements, Gold peak is ~500 ops/cycle)
Ops must match functional unit population
NOT 33 adds!
33 mixed ops including up to 8 adds
issuing: 33 operations

## Slide 10: Which is better?
80% of operations are in loops
Pipelined loops have unbounded ILP
  DSP loops are software-pipelined
But –
  few general-purpose loops can be piped
  (at least on conventional architectures)
Solution:
  pipeline (almost) all loops
  throw function hardware at pipe
Result: loops now < 15% of cycles
33 operations per cycle peak ??? Why?

## Slide 11: Which is better?
33 operations per cycle peak ??? How?
Biggest problem is decode
But that’s another talk!
(Stanford EE380 5/29/2013)
Video, slides and white papers at:
ootbcomp.com/docs/encoding

## Slide 12
Which is better?
33 operations per cycle peak ??? How?
Biggest problem is decode
But the other problem is data
How do you feed data to 30+ operations?
Every cycle?

## Slide 13
Caution
Gross over-simplification!
CPUs are extraordinarily complicated
Designs vary within and between families

## Slide 14
The problem
Lots of data producers (sources):
  168 integer registers
  168 FP/vector registers
  72 load buffers
  ~30 function bypasses
Nearly 500 sources
(x86 Haswell)

## Slide 15
The problem
Lots of data consumers (sinks):
  48 branch buffers
  42 store buffers
  ~16 function arguments
Nearly 100 sinks
(x86 Haswell)

## Slide 16
The problem
sources
sinks
500 X 100 = 50,000

## Slide 17
Meet the multiplexor

## Slide 18
Meet the multiplexor
sources
sinks

## Slide 19
Meet the multiplexor
sources
sinks
Latency proportional to number of levels
Log(number of sources)
Power proportional to number of sources times number of sinks

## Slide 20
The cost
Latency proportional to number of levels
Log(number of sources)
Power proportional to number of sources times number of sinks
log2(500) – 9 levels
40-60% of power
three more pipe stages

## Slide 21
Time for heroics
Latency proportional to number of levels
Log(number of sources)
Power proportional to number of sources times number of sinks
4-to-1 muxes
Multi-port SRAM
Longer pipelines
Power drivers
Partitioning
Helps here and there –
But nothing really works

## Slide 22
Performance limit
Latency proportional to number of levels
Log(number of sources)
Power proportional to number of sources times number of sinks
power/time ceiling for data distribution

## Slide 23
So why have all those sources?
32 program registers, but 300+ rename registers!
Why rename?

## Slide 24
Why rename?
Rt = Ra + Rb
Rx = Rt + 1
Rt = Rc – Rd
Ry = Rt + Re
x = a + b + 1;
y = c – d + e;
Rt1 = Ra + Rb; Rt2 = Rc – Rd
----------------------------
Rx = Rt1 + 1; Ry = Rt2 + Re
Rt = Ra + Rb; Rt = Rc – Rd
--------------------------
Rx = Rt + 1; Ry = Rt + Re
source code
instructions
Hardware renames Rt to Rt1 and Rt2
cycle boundary

## Slide 25
Why does the compiler reuse the temps?
It runs out of temporary registers
There’s no easy way to mark the last use
(or not – the Itanium has over 300 real registers)
(Marking proposals have trouble with control flow)
Registers also used for call arguments
(Don’t know whether callee uses register)

## Slide 26
What are the temps used for?
Of all program-created values:
14% are referenced two or more times
6% are never referenced
80% are referenced exactly once
Registers are purely a naming convention to connect producers with consumers
Registers are a fast memory for frequently referenced local variables
Yale Patt

## Slide 27
So split the uses!
One mechanism for local memory, one for dataflow
Are there any machines that don’t use registers to indicate dataflow?
YES!
Accumulator machine:
Result and one source implicitly addressed
Stack machine
Result and both sources implicitly addressed

## Slide 28
But – no parallelism
5
3
adder
8
stack
Take the top two items on the stack
Add them
And push the result back on the stack
But only one at a time…

## Slide 29
What you really want…
Is several stacks
5
3
8
stack
5
3
6
2
1
stack
4
5
interleaved
3
5
5
8
3
6
2
1
4
5
3
adder
9
that any unit can use

## Slide 30
We call it the Belt
Like a conveyor belt –
a fixed length FIFO
5
8
3
5
3
8
3
3
5
adder
Functional units can read any position
3

## Slide 31
We call it the Belt
3
5
8
5
3
8
3
3
adder
adder
Functional units can read any position
8
New results drop on the front
Pushing the last off the end
3
Like a conveyor belt –
a fixed length FIFO

## Slide 32
Multiple reads
Functional units can read any mix of belt positions
5
8
5
3
8
3
3
adder
8
adder
adder
3
3
3
5
5
3

## Slide 33
Multiple drops
All results retiring in a cycle drop together
8
3
5
5
8
3
8
3
adder
adder
adder
adder
adder
adder
8
8
6

## Slide 34
Belt addressing
Belt operands are addressed by relative position
6
8
5
5
8
3
8
8
b3
b5
“b3” is the fourth most recent value to drop to the belt
“b5” is the sixth most recent value to drop to the belt
This is temporal addressing
add b3, b5
No result address!

## Slide 35
Temporal addressing
The temporal address of a datum changes with more drops
b3
8
3
3
5
5
8
6
8
3
8
8
b6

## Slide 36
Use it or lose it
Compiler schedules producers near to consumers
Nearly all one-use values consumed while on belt
Belt is Single-Assignment - no hazards – no renames
300 rename registers become 8/16/32 belt positions
But - long-lived values must be saved

## Slide 37
The scratchpad
8
8
3
3
6
8
3
8
8
3
belt
scratchpad
spill
3
fill
Frame local – each function has a new scratchpad
Fixed max size, must explicitly allocate
Static byte addressing, must be aligned
Three cycle spill-to-fill latency

## Slide 38
3
Multiple results
2
2
8
8
3
3
6
8
8
3
belt
divide
8
b7
b0
div b0, b7

## Slide 39
Function calls
8
8
3
3
6
8
8
3
Caller’s belt
b7
b0
call func,b1,b5,b3,b3
X
X
X
X
X
X
X
X
Callee’s belt
8
8
3
3
6
8
8
3
0
1
4
9
5
2
7
4
retn b4
2
Caller’s belt
3
6
8
8
A call has the same belt effects as an op like add
A call can drop multiple results

## Slide 40
8
8
3
3
6
8
8
3
Caller’s belt
b7
b0
8
8
3
3
6
8
8
Caller’s belt
2
The Spiller is a background save/restore engine
Values are marked with the owning frame
Belt access is to the values of the current frame
Change the current frame id - the belt is empty!
Data is still there, can be spilled at leisure
Arguments passed by copy, get new frame id
Belt save/restore
Callee

## Slide 41
Function unit pipelines
Each pipeline has two inputs
Shared by several function units
Who share several outputs
adder
shifter
mul’er
There is one output for each result of each latency
Latency-1 result
Latency-3 result

## Slide 42
Function unit pipelines
adder
shifter
mul’er
Latency-1 result
Latency-3 result
lat-1
lat-3
output registers
There is an output register for each latency result that a pipeline produces
Total Mill sources:
All output registers
A few special cases
Minimum 2x belt length
Gold: 64 sources
versus 450

## Slide 43
Wide issue
The Mill is wide-issue, like a VLIW or EPIC
shift
mul
add
PC
slot #
0
1
2
instruction
Instruction slots correspond to function pipelines
Mult’er
shifter
adder
Mult’er
shifter
adder
Mult’er
shifter
adder
pipe #
0
1
2
Decode routes ops to matching pipes
add
shift
mul

## Slide 44
*
Exposed pipeline
Every operation has a fixed latency
a+b – c*d
sub
+
-
a b c d
?
a+b – c*d
c*d
add
mul
a+b
a+b

## Slide 45
Exposed pipeline
Every operation has a fixed latency
add
mul
sub
+
-
a b c d
a+b – c*d
c*d
a+b
a+b – c*d
Who holds this?
*
a+b

## Slide 46
*
Exposed pipeline
Every operation has a fixed latency
add
mul
sub
-
a+b – c*d
c*d
a+b
a+b – c*d
+
a b
c d
Belt usage is best when producers feed directly to consumers

## Slide 47
In-flight over call
muls
call
*
8
8
3
3
6
8
8
3
b7
b0
8
8
3
3
6
8
8
3
in callee
9
in callee
NO!
Should we drop in the middle of the callee?

## Slide 48
8
3
3
6
8
8
2
In-flight over call
muls
call
*
8
8
3
3
6
8
8
3
b7
b0
8
8
3
3
6
8
8
3
9
8
8
3
3
6
8
8
2
8
Calls are atomic
In-flights retire after call returns
(callee)

## Slide 49
Interrupts, traps and faults
These are just involuntary calls
Hardware vectors to the entry point
Hardware supplies the arguments
No doubled state
No task switch
No pipeline flush
No restart penalty after return
A mispredict (4 cycles + cache) is the only delay

## Slide 50
Data forwarding
Not a shift register!
two-stage crossbar
FU
FU
FU
FU
sinks
latency-1 crossbar
ALU
ALU
latency-N crossbar
FPU
shuffle
other…
Back-to-back forwarding cost is one or two muxes
sources
Cost is ~0.3 clock

## Slide 51
Belt timing
FU
FU
FU
FU
latency-1 crossbar
32-bit add
latency-N crossbar
clock boundaries
32-bit mul

## Slide 52
Multiple retires
Each pipeline can issue one operation per clock
The operation will retire latency cycles later
One pipeline!
time

## Slide 53
Multiple retires
Each pipeline can issue one operation per clock
The operation will retire latency cycles later
Ops of different latency can retire together
addb
muls
widenm
addu
retire
To belt
(4-cycle op)
(3-cycle op)
(2-cycle op)
(1-cycle op)

## Slide 54
Belt data location
Each FU pipe has an output register for each latency
Mult’er
shifter
adder
lat-2
lat-1
lat-4
lat-3
add
add
add
add
Now what?

## Slide 55
Belt data location
Each FU pipe has an output register for each latency
Mult’er
shifter
adder
lat-2
lat-1
lat-4
lat-3
add
add
add
add
Now what?
There may be a vacant register in another pipeline
Mult’er
shifter
adder
lat-2
lat-1
lat-4
lat-3

## Slide 56
Belt data location
If there are more latency-registers than belt positions, every live operand has a place to go.
If necessary, add buffer registers.
Other possible implementations:
Register file
CAM
More…
Transparent to software
Choose based on power/clock rate tradeoff, design tools

## Slide 57
Keeping track
The Mill:
Is statically scheduled
Is in-order
Operations execute in program order
The compiler controls when ops issue
Has an exposed pipeline
The compiler knows when ops retire

## Slide 58
Keeping track
The Mill:
Does not rename
Has no general registers
Transient data lives on the Belt
Single-assignment data cannot cause hazards
Has no issue, schedule, or retire stages
Short pipeline; mispredict is 4 + cache cycles

## Slide 59
Keeping track
The Mill:
Naturally handles multi-result ops
Does not encode result addresses
Compact code saves iCache and bandwidth
Simpler for hardware and compiler
Has one operation, one cycle call/return
No prelude or postlude, unlimited arguments

## Slide 60
Want more?
Sign up for technical announcements, white papers, etc.:
ootbcomp.com