## Slide 1
Number six of a series
Drinking from the Firehose
More work in less time -
Mach 3 execution in the Mill™ CPU Architecture

## Slide 2
The Mill CPU
The Mill is a new general-purpose commercial CPU family.
The Mill has a 10x single-thread power/performance gain over conventional out-of-order superscalar architectures, yet runs the same programs, without rewrite.
This talk will explain:
a review of the Belt, the replacement for general registers
phasing, a 3x average speedup of dependent operations
ganging, when operations need more arguments
sidekick predicates, to speed up conditional branches
First Winner Rule, for N-way branching
cascaded calls, phasing across call/return

## Slide 3
Talks in this series
Encoding
The Belt
Memory
Prediction
Metadata and speculation
Execution
Security
Threading
You are here
Slides and videos of other talks are at:
ootbcomp.com/docs

## Slide 4
addsx(b2, b5)
The Mill Architecture
Execution
New with the Mill:
Instructions issue over more than one clock
Dataflows within an instruction
Operations using two issue pipelines
Removing the two-argument limit
Speculable condition codes
Extra bool results without delay or hazard
Concurrent N-way branches
Fast complex predicates
Cascaded calls in one instruction
Hardware-assisted tail calls

## Slide 5
Caution!
Gross over-simplification!
This talk tries to convey an intuitive understanding to the non-specialist.
The reality is more complicated.
(we try not to over-simplify, but sometimes…)

## Slide 6
A review
The Belt
The Mill is a belt machine.
There are no general registers.

## Slide 7
We call it the Belt
Like a conveyor belt –
a fixed length FIFO
5
8
3
5
3
8
3
3
5
adder
Functional units can read any position
3

## Slide 8
We call it the Belt
3
5
8
5
3
8
3
3
adder
adder
Functional units can read any position
8
New results drop on the front
Pushing the oldest off the end
3
Like a conveyor belt –
or a fixed length FIFO

## Slide 9
Multiple reads
Functional units can read any mix of belt positions
5
8
5
3
8
3
3
adder
8
adder
adder
3
3
3
5
5
3

## Slide 10
Multiple drops
All results retiring in a cycle drop together
5
5
8
3
8
adder
adder
adder
adder
adder
adder
8
8
6
8
3
3

## Slide 11
Belt addressing
Belt operands are addressed by relative position
6
8
5
5
4
3
8
8
b3
b5
“b3” is the fourth most recent value to drop to the belt. “b5” is the sixth most recent value to drop to the belt.
This is temporal addressing
add b3, b5
No result address!

## Slide 12
Temporal addressing
The temporal address of a datum changes with more drops
b3
8
3
3
5
5
8
6
8
3
8
8
b6

## Slide 13
Data-dependent operations
phasing
Executing faster than the clock rate.

## Slide 14
Data-dependent operations
A dataflow is a sequence of operations in which each uses the prior result. When there are no inter-operation delays then the dataflow is executing at Mach 1.
a = b + 12345678;
const
add
store
source code:
machine code:
store
add
const
cycle boundary

## Slide 15
Data-dependency in VLIWs
A VLIW is a wide-issue machine that can issue several operations per instruction. All operations in an instruction execute in parallel.
a = b + 12345678;
const add store
source code:
machine code
store
add
const
cycle boundary
Possible? Unfortunately, no such luck.

## Slide 16
Data-dependency in the Mill
The Mill splits each execution cycle into phases.
a = b + 12345678;
const add store
source code:
machine code
store
add
const
cycle boundary
phase boundary
Operations in different phases can be part of a dataflow
This is the logical view as seen by the program.
Physical reality is different.

## Slide 17
Operation phasing
Phases execute in sequence as a dataflow.
Each operation is defined to execute in a particular phase.
Each op can see results that retired in the prior phases.
phase
typical op functions
readerPhase
opPhase
callPhase
pickPhase
writerPhase
constants, scratchpad read
add, load, equal, etc.
function calls
pick (a?b:c)
store, branches, scratchpad write
const add store
readerPhase
opPhase
writerPhase

## Slide 18
Phases spread across cycles
Ops from one instruction issue over three different cycles.
readerPhase
opPhase
writerPhase
instruction 1
instruction 2
instruction 3
readerPhase
opPhase
writerPhase
readerPhase
opPhase
writerPhase
Phases form an intra-instruction software pipeline

## Slide 19
Phase assignment
Operations are assigned to phases in typical dataflow order.
readerPhase
opPhase
writerPhase
Pure sources, with no inputs
Ops with both inputs and results
Pure sinks, with no results
Because there are cycle boundaries between these phases, the result of each phase can be passed to the next phase, in the following cycle.

## Slide 20
decoder
execute
Phasing and decode
The Mill decoders are fully pipelined and can start decode of a new instruction every cycle.
microcache

## Slide 21
execute
Phasing and decode
Mill instructions encode in six blocks of zero or more ops.
Two of the blocks decode a cycle before the others.
All ops assigned to readerPhase are in the early blocks.
decoder
inst 1
reader phase
ops phase
writer phase
reader
ops
writer

## Slide 22
decoder
execute
Phasing and decode
The Mill decoders are fully pipelined and can start decode of a new instruction every cycle.
reader
ops
writer
inst 1
inst 2
inst 3
reader
ops
reader
ops
inst 4
writer
writer
reader
ops
writer
Phases of one instruction overlap the phases of adjacent instructions.
Reader phase of one instruction happens in the same cycle as ops phase of the prior instruction and the writer phase of the one before that.

## Slide 23
Other phases – pick phase
Pick phase is used by the pick operation, which implements the triadic predicate operation (a?b:c).
Pick does not use a functional unit. Instead it is implemented in the bypass crossbar, that routes operand results of one cycle to functional unit inputs of the following cycle.
store
x = a==0 ? b : c;
source code:
eql
a
0
pick
b
c
x
opPhase
pickPhase
writerPhase

## Slide 24
Other phases – call phase
Call phase is used only by the call operation.
The function call occurs after prior phases (if any).
Remaining phases (if any) are executed after return.
source code:
x = f(a+b);
machine code:
add call store
add
?
retn
store
in called function
After a return, the instruction containing the call is re-executed, but without the operations that were already issued.

## Slide 25
Cascaded calls
A Mill instruction may have more than one call operation.
Multiple calls are executed consecutively, in slot order.
Returns transfer directly to the next called function.
source code:
x = F(G(a+b));
machine code:
add call call store
add
F retn
store
in called function G
G retn
in called function F
direct transfer

## Slide 26
The impact of phasing
Conventional CPU design has abandoned the quest for operation-level parallelism because of a belief that open code has OLPs of only 2 or 3. This belief is false.
This is Mach 3
source code:
a = b + 12345; c = d – 54321;
con con
add sub
store store
OLP is 2, three cycles
conventional:
Mill
con con add sub store store
OLP is 6, one cycle

## Slide 27
Where the gain is
In long basic blocks, phasing offers no improvement over conventional VLIW.
other ops in BB
Mill phasing
VLIW, no phasing
A VLIW scheduler can put the phased ops in the instructions that issue in the cycle when a phase would issue on the Mill.
…
<ops>
<ops>
<ops>
<ops>
…
…
<ops>
<ops>
<ops> con add store
<ops>
…
…
<ops>
<ops> con
<ops> add
<ops> store
…
con
store

## Slide 28
Where the gain is
When adjacent to control flow, phasing saves cycles over conventional VLIW.
Mill, with phasing
VLIW, no phasing
brtr
con add store brfl
<ops>
con
store
only if taken
taken or not
brtr
<ops>
only if taken
taken or not
con
add
store brfl
Mill phases are in effect moved over control flow.
A VLIW scheduler cannot move ops over control flow or they would execute on both paths.

## Slide 29
Where the gain is
Phasing, like out-of-order, approximates Dataflow.
  You can think of phasing as statically-scheduled OOO.
Phasing beats VLIW only when adjacent to control flow.
  But control flow is frequent – every 6 to 10 operations.
OOO beats phasing when dependencies are not in phase order.
  With phasing, F(a+b) is one cycle, but a+F(b) is two.
Phasing beats OOO when OOO is issue-limited.
  Mill is wide enough that issue is not a constraint.
Phasing, like deferred loads, lets the Mill have OOO performance without the huge power and area cost.

## Slide 30
Special operation formats
ganging
Removing a source-count limitation.

## Slide 31
Special operation formats
Nearly all operations have a two-in one-out structure.
add
belt
Operations are encoded, and data-paths within the CPU are allocated, to optimize this common case.
Unfortunately, there are exceptions.

## Slide 32
Fused multiply-add (FMA)
FMA is annoying; it has three inputs and computes a*b+c.
A third input to the encoding and a third datapath to the function pipeline would be expensive!
FMA
belt
Kludges abound.

## Slide 33
Ganging FMA
A gang comprises two or more adjacent two-input pipelines that cooperatively implement a single operation.
FU
FU
Each pipeline has a normal encoding slot and contains ordinary two-input functional units such as ALUs and FPUs.

## Slide 34
Ganging FMA
A gang comprises two or more adjacent two-input pipelines that cooperatively implement a single operation.
belt
The Mill defines a new operation “args” with no result.
It passes its inputs horizontally to the next lower slot.
FMA
args

## Slide 35
Ganging FMA
A gang comprises two or more adjacent two-input slots that cooperatively implement a single operation.
belt
FMA
args
Ganging is used for all operations that need more than two arguments.

## Slide 36
Ganging FMA
This seems wasteful – a whole slot used for nothing but passing an argument. What’s really going on?
belt
FMA
args

## Slide 37
mul
add
Ganging FMA
This seems wasteful – a whole slot used for nothing but passing an argument. What’s really going on?
belt
args
But we can put the second slot to work.

## Slide 38
mul
add
Ganging FMA to make FMAS
By adding a fourth input, the function units of the second slot can be combined with the FMA.
belt
mul
sub
The Mill FMAS (fused multiply-add-subtract) operation computes the sum and difference of two products.

## Slide 39
mul
add
Or two FMAs instead
An args operation with two inputs can feed the same hardware to get two FMA operations instead of FMAS.
belt
mul
add
FMAS has only one rounding error; it is more precise than the equivalent FMA sequence.
args

## Slide 40
Speculable condition codes
predicate gangs

## Slide 41
Speculable condition codes
Condition codes are implicit additional Boolean results of arithmetic operations. They carry predicate metadata about the primary result: is it less than, equal to or greater than zero; did the arithmetic cause an overflow, or produce a carry; etc.
source code:
if (--i > 0) {…}
machine code:
subtract
gtr
branch true
subtract
branch gtr
without CC:
with CC:
But -
Codes rarely used
Almost always immediately consumed
Codes cannot be speculated

## Slide 42
Speculable condition codes
source code:
if (--i > 0) {…}
machine code:
subtract
gtr
branch true
subtract
branch gtr
without CC:
with CC:

## Slide 43
one instruction
Speculable condition codes
source code:
if (--i > 0) {…}
machine code:
subtract
gtr
branch true
subtract
branch gtr
without CC:
with CC:
Mill code:
subtract gtr brtr
subtract
gtr brtr
opPhase opPhase writerPhase
two instructions

## Slide 44
How about two results?
The Belt makes multi-result operations easy.
Define subtract-gtr to return both the difference and a bool.
source code:
if (--i > 0) {…}
Mill code:
subtract-gtr brtr
opPhase writerPhase
But -
Huge opcode explosion – sub-lss, add-gtr, etc.
Requires another fastpath – clock impact

## Slide 45
The solution: ganging predicate tests
ALUs provide condition-code signals to the adjacent slot.
Define gtr_code to return the received code as a result.
source code:
if (--i > 0) {…}
Mill code:
subtract gtr-code brtr
opPhase writerPhase
brtr
sub
gtr
code
Predicates are speculable, like any belt operand.
gang
All one instruction
phasing!

## Slide 46
Multi-way branches
first winner rule

## Slide 47
Multi-way branches
Switch (case) statements are often annoying in hardware.
source code:
switch (i) {
case 3: …;
case 5: …;
default: …
}
machine code:
eql i, 3
brtr case3
eql i, 5
brtr case5
default:
Problems:
Branches execute sequentially.
Entries for each branch clutter prediction tables.
Sequence may mispredict several times.

## Slide 48
Multi-way branches
The Mill supports multi-way branching.
source code:
switch (i) {
case 3: …;
case 5: …;
default: …
}
Mill code:
eql(i, 3) brtr(case3) eql(i, 5) brtr(case5);
machine code:
eql i, 3
brtr case3
eql i, 5
brtr case5
default:
Branches in one instruction execute in parallel.
First taken branch in slot order wins (First Winner Rule).
Only one prediction for whole switch.
No more than one misprediction is possible.
opPhase writerPhase opPhase writerPhase

## Slide 49
Summary #1:
The Mill:
Issues single instructions over three cycles
Permits intra-instruction dataflow
Can increase open-code ILP 7x+; 3x typical
Pseudo-OOO executes operations over control flow
Supports instructions with multiple calls
Data flows may contain one of more calls

## Slide 50
Summary #2
The Mill:
N-way branching in one instruction
Automatically tail-calls cascaded calls
Last in cascade returns to original instruction
“First” taken branch wins
Not constrained by pipeline datapaths
Permits novel {M -> N} operations

## Slide 51
Summary #3
The Mill:
Has speculable condition-codes
Performance gain without global state

## Slide 52
Shameless plug
For technical info about the Mill CPU architecture:
ootbcomp.com/docs
To sign up for future announcements, white papers etc.
ootbcomp.com/mailing-list