## Slide 1
Stanford EE380 5/29/2013
Drinking from the Firehose
Decode in the Mill™ CPU Architecture

## Slide 2
addsx(b2, b5)
The Mill Architecture
Instructions -
Format and decoding
New to the Mill:
Dual code streams
No-parse instruction shifting
Double-ended decode
Zero-length no-ops
In-line constants to 128 bits

## Slide 3: Two architectures
cores: 1 core
issuing: 8 operations
clock rate: 456 MHz
power: 1.1 Watts
performance: 3.6 Gips
price: $17 dollars
cores: 4 cores
issuing: 4 operations
clock rate: 3300 MHz
power: 130 Watts
performance: 52.8 Gips
price: $885 dollars
in-order VLIW DSP
out-of-order superscalar
406 Mips/W
59 Mips/$
3272 Mips/W
211 Mips/$

## Slide 4: Two architectures
in-order VLIW DSP
out-of-order superscalar
406 Mips/W
59 Mips/$
3272 Mips/W
211 Mips/$
3.6X better performance
30X more power
13X more money
Comparison per core

## Slide 5: Which is better?
DSP efficiency
- on general-purpose workloads
Why huge cost in both power and price?
32 vs. 64 bit
3,600 mips vs. 52,800 mips
incompatible workloads
signal processing ≠ general-purpose
goal – and technical challenge:

## Slide 6
Our result:
cores: 2 cores
issuing: 33 operations
clock rate: 1200 MHz
power: 28 Watts
performance: 79.3 Gips
price: $225 dollars
OOTBC Mill Gold.x2
2832 Mips/W
352 Mips/$
Clock, power: our best estimate after several years in sim
Price: wild guess

## Slide 7
Our result
vs. OOO superscalar:
vs. VLIW DSP:
2.3X more performance
2.3X less power
1.9X less money
11x more performance
12X more power
6.5X more money
OOTBC Mill Gold.x2
2832 Mips/W
352 Mips/$
Comparison per core

## Slide 8
Our result:
cores: 2 cores
issuing: 33 operations
clock rate: 1200 MHz
power: 28 Watts
performance: 79.3 Gips
price: $225 dollars
OOTBC Mill Gold.x2
2832 Mips/W
352 Mips/$

## Slide 9
Caution!
issuing: 33 operations
33 independent MIMD operations
NOT counting each SIMD vector element!
(counting elements, Gold does ~500 ops/cycle)
Ops must match functional unit population
NOT 33 adds!
33 mixed ops including up to 8 adds

## Slide 10: Which is better?
80% of code is in loops
Pipelined loops have unbounded ILP
  DSP loops are software-pipelined
But –
  few general-purpose loops can be piped
  (at least on conventional architectures)
Solution:
  pipeline (almost) all loops
  throw function hardware at pipe
Result: loops now < 15% of cycles
33 operations per cycle peak ??? Why?

## Slide 11: Which is better?
33 operations per cycle peak ??? How?
Biggest problem is decode
Fixed length instructions:
Easy to parse
Instruction size:
32 bits X 33 ops = 132 bytes.
Ouch!
Instruction cache pressure.
32k iCache = only 248 instructions
Ouch!!

## Slide 12
Which is better?
33 operations per cycle peak ??? How?
Biggest problem is decode
Variable length instructions:
Hard to parse – x86 heroics gets 4 ops
Instruction size:
Mill ~17 bits X 33 ops = 70 bytes.
Ouch!
Instruction cache pressure.
32k iCache = only 537 instructions
Ouch!!

## Slide 13
A stream of instructions
inst
inst
inst
inst
inst
inst
inst
Program
counter
decode
execute
inst
inst
inst
inst
inst
inst
inst
Program
counter
decode
execute
execute
execute
bundle
Logical model
Physical model

## Slide 14
Fixed-length instructions
inst
inst
inst
inst
Program
counter
decode
execute
decode
decode
inst
execute
execute
Are easy!
(and BIG)
bundle

## Slide 15
Variable-length instructions
inst
inst
inst
inst
Program
counter
decode
execute
decode
decode
inst
execute
execute
Where does the next one start?
Polynomial cost!
?
?
?
bundle

## Slide 16
OK if N=3, not if N=30
BUT…
Two bundles of length N are much easier than one bundle of length 2N
Polynomial cost
So split each bundle in half, and have two streams of half-bundles
inst
Program
counter
bundle
inst
inst
inst
inst
inst
inst
inst
inst
inst
inst
inst

## Slide 17
Two streams of half-bundles
inst
Program
counter
half bundle
inst
inst
inst
inst
inst
inst
inst
inst
inst
inst
inst
inst
Program
counter
half bundle
inst
inst
inst
inst
inst
inst
inst
inst
inst
inst
inst
decode
execute
decode
Two physical streams
One logical stream
But – how do you branch two streams?

## Slide 18
Extended Basic Blocks (EBBs)
EBB
branch
EBB
Program
counter
EBB
EBB
EBB
EBB
EBB
EBB chain
EBB chain
Group each stream into Extended Basic Blocks, single-entry multiple-exit sequences of bundles.
Branches can only target EBB entry points; it is not possible to jump into the middle of an EBB.
Program
counter

## Slide 19
Take two half-EBBs
bundle
bundle
bundle
bundle
EBB head
bundle
bundle
bundle
bundle
EBB head
execution order
lower
addresses
higher
addresses

## Slide 20
bundle
bundle
bundle
bundle
EBB head
bundle
bundle
bundle
bundle
EBB head
bundle
bundle
bundle
bundle
EBB head
execution order
Reverse one in memory
Two halves of each instruction have same color
execution order
execution order
lower
addresses
higher
addresses

## Slide 21
bundle
bundle
bundle
bundle
EBB head
bundle
bundle
bundle
bundle
EBB head
And join them head-to-head
lower
addresses
higher
addresses

## Slide 22
And join them head-to-head
bundle
bundle
bundle
bundle
EBB head
bundle
bundle
bundle
bundle
EBB head
entry point
lower
addresses
higher
addresses

## Slide 23
bundle
bundle
bundle
bundle
bundle
bundle
bundle
bundle
entry point
Take a branch…
…
add …
load …
jump loop
Effective address
lower
addresses
higher
addresses

## Slide 24
bundle
bundle
bundle
bundle
bundle
bundle
bundle
bundle
entry point
Take a branch…
…
add …
load …
jump loop
Effective address
program
counter
program
counter
lower
addresses
higher
addresses

## Slide 25
bundle
bundle
bundle
bundle
bundle
bundle
bundle
bundle
Take a branch…
program
counter
program
counter
decode
decode
execute
bundle
bundle
bundle
bundle
bundle
bundle
bundle
bundle
higher
addresses
lower
addresses

## Slide 26
bundle
bundle
bundle
bundle
bundle
bundle
bundle
bundle
Take a branch…
program
counter
program
counter
decode
decode
execute
bundle
bundle
bundle
bundle
bundle
bundle
higher
addresses
lower
addresses

## Slide 27
bundle
bundle
bundle
bundle
bundle
bundle
bundle
Take a branch…
program
counter
program
counter
decode
decode
execute
bundle
bundle
bundle
bundle
bundle
higher
addresses
lower
addresses

## Slide 28: After a branch
EBB entry point
cycle 0
cycle n
Program counters:
XPC = Exucode
FPC = Flowcode
XPC moves forward
FPC moves backwards
Transfers of control set both XPC and FPC to the entry point
Exu code
Flow code
memory
FPC
XPC
memory
FPC
XPC
increasing addresses
increasing addresses

## Slide 29: Physical layout
iCache
decode
exec
critical distance
iCache
decode
exec
critical distance
iCache
decode
critical distance
iCache
decode
exec
critical distance
Mill
Conventional

## Slide 30
header
block 1
block 2
block n
byte boundary
alignment hole
byte boundary
variable length blocks
Generic Mill bundle format
block n-1
The Mill issues one bundle (two half-bundles) per cycle.
That one bundle can call for many independent operations, all of which issue together and execute in parallel.
Each half-bundle begins with a fixed-format header.
Blocks contain variable numbers of bit-aligned operations
All operations in a block use the same format.
Header has byte count for bundle, op count for each block.
Parsing reduces to isolating blocks.
Half-bundle format

## Slide 31
Generic instruction decode
cycle 1
byte boundary
header
Bundle buffer
block 1
block 3
block 2
hole
# bytes
Header format
block1 cnt
(assumes 3 blocks)
operation blocks
block2 cnt
block 1
Block 1 decode
header

## Slide 32
Generic instruction decode
cycle 1
byte boundary
header
Bundle buffer
block 1
block 3
block 2
hole
block 1
header
shifter
block 2
Block 2 buffer

## Slide 33
hole
Generic instruction decode
cycle 1
byte boundary
Bundle buffer
block 3
header
block 2
hole
block 1
header
block 2
bundle shifter
blocks
header
Block 2 buffer

## Slide 34
hole
Generic instruction decode
cycle 2
byte boundary
Bundle buffer
block 3
header
block 2
Block 2 decode
blocks
header
Block 3 decode
block 2
block 3
Block 2 buffer
cycle 1

## Slide 35
Block 2 buffer
hole
Generic instruction decode
cycle 2
byte boundary
Bundle buffer
block 3
header
block 2
blocks
header
block 2
block 3
Bundles are parsed from both ends
Decode 2N+1 blocks in N cycles

## Slide 36
Elided No-ops
Exucode:
Flowcode:
head
op
0
op
head
op
2
op
head
op
1
op
head
op
0
op
hole
head
op
0
op
head
op
0
op
head
op
0
op
hole
head
op
0
op
head
op
0
op
head
op
0
op
Sometimes a cycle has work only for Exu, only for Flow, or neither. The number of cycles to skip is encoded in the alignment hole of the other code stream.
Rarely, explicit no-ops must still be used when there are not enough hole bits to use. Otherwise, no-ops cost nothing.
- - -
- - -
- - -

## Slide 37: Mill pipeline
prefetch
mem/L2
L1 I$
fetch
L0 I$
decode
lines
shifter
issue
bundles
execute
operations
results
retire
reuse
phase/cycles
D0
D0-D2
X0-X4+
<none>
<none>
F0-F2
<varies>
4 cycle mispredict penalty from top cache

## Slide 38: Split-stream, double-ended encoding
Two program counters
Following two instruction half-bundle streams
Drawn from two instruction caches
Feeding two decoders
One of which runs backwards
And each half-bundle is parsed from both ends
One Mill thread has:
For each side:
Bundle size:
Mill ~17 bits X 17 ops = 36 bytes
Instruction cache pressure.
32k iCache = 1024 instructions
Decode rate:
30+ operations per cycle

## Slide 39
Want more?
Sign up for technical announcements, white papers, etc.:
ootbcomp.com