## Slide 1
Number three of a series
Drinking from the Firehose
Mostly missless memory
in the Mill™ CPU Architecture
LTCG
LTCG

## Slide 2
Talks in this series
Encoding
The Belt
Cache hierarchy
Prediction
Metadata and execution
Specification
…
You are here
Slides and videos of other talks are at:
ootbcomp.com/docs

## Slide 3
addsx(b2, b5)
The Mill Architecture
Cache access-
- without delay
New with the Mill:
No store misses
No store buffers needed
Cache latency is hidden
Most loads have zero apparent latency
Backless memory
Transient memory needs no OS intervention
No init, no load, and no writeback stack frames
Clean and exploit-free
Sequential consistency throughout
Simpler concurrent programming

## Slide 4
Caution
Gross over-simplification!
CPUs are extraordinarily complicated
Designs vary within and between families

## Slide 5
When loads miss…
deferred loads

## Slide 6
The market wants…
High execution throughput
Low power
Low cost
How to achieve this has been known for forty years.
  wide-issue: many operations issue and execute each cycle.
  statically scheduled : the compiler determines when each operation begins.
  exposed pipeline: operation results are not returned at once, but after a known latency.
You can buy such a chip today.
The Mill works the same way.

## Slide 7
shift
mul
Wide issue
The Mill is wide-issue, like a VLIW or EPIC
mul
shift
add
PC
slot #
0
1
2
instruction
Instruction slots correspond to function pipelines
mult’er
shifter
adder
mult’er
shifter
adder
mult’er
shifter
adder
pipe #
0
1
2
Decode routes ops to matching pipes
add

## Slide 8
*
Exposed pipeline
Every operation has a fixed latency
a+b – c*d
sub
+
-
a b c d
a+b
?
a+b – c*d
c*d
a+b
add
mul

## Slide 9
Exposed pipeline
Every operation has a fixed latency
add
mul
sub
+
-
a b c d
a+b
a+b – c*d
c*d
a+b
a+b – c*d
Who holds this?
*

## Slide 10
*
Exposed pipeline
Every operation has a fixed latency
add
mul
sub
-
a+b – c*d
c*d
a+b
a+b – c*d
+
a b
c d
Code is best when producers feed directly to consumers
Static scheduling

## Slide 11
Exposed pipeline machines deliver their performance throughput only when all operation have a statically (compiler) known latency.
If latencies can vary, the compiler must assume the common case.
If the compiler is wrong, then all instruction issue stalls until the operation is done.
Ouch!
The catch
In practice the only varying-latency operation that matters is load.

## Slide 12
The memory hierarchy
load
D$1
D$2
DRAM
~3 cycles
~10 cycles
~300+ cycles

## Slide 13
The load problem
load
add
shift
store
stall
You write:
add
load
shift
store
You get:
stall
stall
stall
Every architecture must deal with this problem.

## Slide 14
Every CPU’s goal – hide load latency
General strategy:
Issue loads as early as possible
    - as soon as the address is known
    - or even earlier – aka prefetch
Find something else to do while waiting for data
    hardware approach – dynamic scheduling Tomasulo algorithm on IBM 360/91 (1967)
    - software approach – static scheduling exposed pipeline, delay slots
Ignore program order: issue operations as soon as their data is ready

## Slide 15
Hardware approach – dynamic scheduling
Hardware:
decodes ahead, buffering decoded instructions
tracks operations whose data is not ready
issues ready operations when hardware available
at operation retire, updates waiting operations with result
The good:
  Can hide cache latency and misses so long as there is any other work to do
The bad:
  Window-limited; can only issue already-decoded instructions
The ugly:
  Extremely expensive in area and power

## Slide 16
Software approach – static scheduling
Compiler:
determines dependencies among operations
schedules producer retire just before consumer issue
schedules independent operations to issue together
schedules loads as if they hit in level 1 cache
The good:
  Cheap, low power, fast hardware
  No window limit, can schedule from whole program
The bad:
  Limited load concurrency
The ugly:
  A cache miss stalls all instruction issue

## Slide 17
Several different load problems…
Some loads will always miss to DRAM.
Random access to a huge hash table runs at DRAM speed.
Some loads must wait for data-dependent addressing.
“Smart memory” proposals for linked-list chaining have failed.
No CPU architecture has a good solution for these.
Nor the Mill either.

## Slide 18
Several different load problems…
Some loads depend on control flow.
if(a && b) – can’t load b until a is resolved.
This isn’t a load problem
It’s a speculation problem.
Mill speculation is the subject of a future talk in this series.
Sign up for talk announcements at:
ootbcomp.com/mailing-list

## Slide 19
Several different load problems…
Some loads form related groups with regular addressing.
Iterating over an array is typical.
This isn’t a load problem
It’s a prefetch problem.
Mill prefetching is the subject of a future talk in this series.
Sign up for talk announcements at:
ootbcomp.com/mailing-list

## Slide 20
Several different load problems…
Some loads come in independent bunches
a+b+c – needs multiple concurrent loads
Some loads miss in D$1 and hit in D$2
needs a way to hide unexpected delay
What’s left?
Out-of-order hardware handles these cases.
Only these cases.
“The dirty little secret of out-of-order is how little out-of-order there really is”
Andy Glew

## Slide 21
Mill “deferred loads”
load(
Generic Mill load operation:
address: 64-bit base; offset; optional scaled index
width: scalar 1/2/4/8/16 byte, or vector of same
delay: number of issue cycles before retire
load(…, …, 4)
instruction
instruction
instruction
instruction
consumer
load issues here
data available here
<address>
, <width>
, <delay>)
retire is deferred for four instructions
load retires here

## Slide 22
retire
retire
retire
Deferred loads vs. alternatives
static:
deferred:
load
no-op
no-op
load(,,2)
no-op
no-op
When there’s nothing to do but wait:
Mill no-ops occupy no extra space in the code stream.
Details in ootbcomp.com/docs/encoding
dynamic:
load
stall
stall
All three have same performance
(assumes no independent ops available)

## Slide 23
load(,,5)
op1
op2
op3
op4
op5
load
op1
op2
op3
op4
op5
retire
retire
retire
Deferred loads vs. alternatives
static:
deferred:
With ops to hide the D$1 latency, and a hit:
dynamic:
load
op1
op2
op3
op4
op5
All three have same performance
(assumes five independent ops available)

## Slide 24
load
op1
op2
stall
stall
stall
op3
load(,,5)
op1
op2
op3
op4
op5
op6
load
op1
op2
op3
op4
op5
op6
retire
retire
retire
Deferred loads vs. alternatives
static:
deferred:
With ops to hide the D$1 latency, and a miss:
dynamic:
Deferred same as dynamic, beats static
(assumes five independent ops available)

## Slide 25
Reordering can hide more stalls
The program may be re-written to change the operation order, or the compiler or hardware may re-order ops if the change preserves the semantics of program order.
Loads may be hoisted over prior operations
Consumers may be lowered over later operations.
op1
op2
op3
load
consumer
hides one stall
hides three stalls
hides two stalls

## Slide 26
Reordering constraints
Can’t hoist a consumer over its producer
- must preserve dataflow partial order
Producers can communicate with consumers via memory
- cannot hoist a load over a store to same address
Hardware knows if it’s the same address, an alias
Compiler often cannot tell if load and store are aliases
- must assume worst case
- static schedules suffer from false aliasing

## Slide 27
The instruction:
load(a,,7)
means:
“Give me the value of a seven instructions from now”.
It also means:
“Give me the value as it will be after seven instructions”.
So eliminate aliasing
A load sees memory as-of some point in its execution. It sees the effect of stores from before that point, and does not see the effect of stores after that point
Mill loads see memory as of retire.

## Slide 28
Alias immunity
In the Mill, load issue may be hoisted over stores, including stores that alias.
op1
op2
store
op3
store
op4
load
consumer
op1
op2
store
op3
store
op4
load
consumer
retire
retire
Same semantics; same value loaded
Even if a store is to same address
(,,6)
original:
as modified:

## Slide 29
Loads across control flow
Loads may be deferred across control flow, so long as the latency is statically fixed.
load(,,9)
<then>
(6 cycles)
<else>
(6 cycles)
consumer
retire here
load(,,9)
<then>
(6 cycles)
<else>
(3 cycles)
consumer
or here
retire here
Oops!

## Slide 30
Pickup loads
load(
Generic Mill pickup load operation:
address: 64-bit base; offset; optional scaled index
width: scalar 1/2/4/8/16 byte, or vector of same
name: user-selected identifier
load(…, …, t5)
<instruction>
<instruction>
pickup(t5)
consumer
load issues here
<address>
, <width>
, <name>)
retire deferred until matching pickup executed
load retires here

## Slide 31
Compiler strategy
Schedule in time reversed order, consumers first.
Schedule producers to retire just before first consumer.
Schedule from longest-latency dataflow first
  gives shortest latency schedule overall
Hoist load issue to the address producer.
Add no-ops to pad to D$1 latency if necessary.
Set the delay argument of the loads.

## Slide 32
The trade-off
Out-of-order
Static scheduling
Can hide parts of some misses
Immune to false aliasing
Complex, power hungry hardware
A miss stalls all instruction issue
Cannot resolve false aliasing
Simple, economical hardware

## Slide 33
A miss stalls all instruction issue
Cannot resolve false aliasing
Simple, economical hardware
The tradeoff
Out-of-order
Static scheduling
Can hide parts of some misses
Immune to false aliasing
Complex, power hungry hardware
Can hide same misses as out-of-order
Immune to false aliasing
Simple, economical hardware
The Mill

## Slide 34
Implementation – the retire station
Each Mill family member has a configured number of hardware retire stations.
address
width
counter
data buffer
The load operation:
  allocates a station
  unpacks the arguments
  sends a request to the memory hierarchy
load(<address>,<width>,<delay>)
<address>,
0x123…
<width>
<delay>
double
7
-----------------

## Slide 35
Implementation – stream monitoring
store unit
request
D$1 cache
active retire stations
Store functional units convert store operations into requests forwarded to the top data cache.
Active retire stations monitor the stream of requests for overlapping addresses.
inactive stations

## Slide 36
Implementation – stream monitoring
store unit
request
D$1 cache
active retire stations
Store functional units convert store operations into requests forwarded to the top data cache.
Active retire stations monitor the stream of requests for overlapping addresses.
On a hit, the station discards buffered data and re-requests the load data.
inactive stations

## Slide 37
Retire station allocation
Stations are frame-local: each function (logically) has its own.
Physical stations are dynamically allocated. Loads from different frames may be in-flight concurrently.
frame
frame
frame
Non-local stations are spilled if necessary.
to spiller
Only the address and size are spilled. return re-requests any spilled loads.

## Slide 38
The fine print #1
There are a few rare cases in which a hardware dynamic scheduler can avoid some stall cycles that the Mill cannot; these cases mostly involve cascaded dependent loads.
In balance, the Mill compiler can examine much more of the program when looking for independent operations than can the window-bound hardware dynamic scheduler.
The two effects are both minor and offsetting, so to a first approximation the Mill provides the same memory performance as does out-of-order hardware, at greatly reduced cost in power and area.

## Slide 39
The fine print #2
A retire station that is spilled across a function call or task switch is reallocated on return or revisit and the original load is in effect re-issued to the cache hierarchy.
The original load will have caused a DRAM value to have been brought into cache while the function was executing, so usually the repeated load request will be satisfied from cache, not DRAM.
The branch prediction logic can anticipate return operations and can give the spiller advance notice. This permits load reissue in advance of the actual return, thereby masking cache latency of the re-issued load.

## Slide 40
When stores miss…
valid bits

## Slide 41
When the program writes to a line not in cache, traditional architectures either…
  write the new data direct to DRAM (write-through)
or…
  read the line from DRAM, then update it (write-back)
When stores miss…
Either way, the store must be buffered, and later loads and stores to the same line must be detected and merged. With a hundred or more loads and stores in flight concurrently, the hardware and power cost is extreme.
Not on a Mill.

## Slide 42
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
Valid bits
Every byte in every Mill cache line has eight bits of data and one “valid” bit. A store sets the valid bits.
store(a, “hello, w”)
(not actual syntax)
h
e
l
l
o
,
w
hello, w
D$1 cache line

## Slide 43
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
Valid bits
Every byte in every Mill cache line has eight bits of data and one “valid” bit. A store sets the valid bits.
store(a, “hello, w”)
store(a+8, “orld! ”)
(not actual syntax)
orld!
o
r
l
d
!
D$1 cache line
D$2 cache line
Interrupt!
h
e
l
l
o
,
w
X
X
X
X
X
X
X
X
X
X
X
X
X

## Slide 44
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
h
e
l
l
o
,
w
X
X
X
X
X
X
X
X
X
X
X
X
X
Valid bits
Load requests contain a mask of the desired bytes
load(a+4,,)
o
r
l
d
!
D$1 cache line
D$2 cache line
retire station
o
r
l
d
request

## Slide 45
h
e
l
l
o
,
w
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
Bytes that are both requested and valid are copied to the retire station.
Valid bits
load(a+4,,)
o
r
l
d
!
D$1 cache line
D$2 cache line
retire station
o
r
l
d

## Slide 46
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
Valid bits
Unsatisfied requests are forwarded down one level.
load(a+4,,)
o
r
l
d
!
D$1 cache line
D$2 cache line
retire station
o
r
l
d
h
e
l
l
o
,
w
X
X
X
X
X
X
X
X
X
X
X
X
X

## Slide 47
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
Valid bits
Any line that is “hit” is copied up one level, and merged if the line is also there; top valid byte wins.
load(a+4,,)
D$1 cache line
D$2 cache line
retire station
o
r
l
d
o
,
w
Unsatisfied requests are forwarded down one level.
h
e
l
l
o
,
w
X
X
X
X
X
X
X
X
X
X
X
X
X
h
e
l
l
o
,
w
X
X
X
X
X
X
X
X
X
X
X
X
X
o
r
l
d
!

## Slide 48
When the OS costs too much…
backless memory

## Slide 49
Hierarchy from 40,000 ft.
load/store FUs
retire stations
CPU core
decode
I$0e
I$0f
D$1
I$1e
L$2
Harvard level 1
shared level 2
DRAM
ROM
MMIO
device controllers
devices
I$1f
iPLB
TLB
dPLB
View is representative. Actual hierarchy is configured in each chip specification.
The Mill uses virtual caching and the single address space model.

## Slide 50
Hierarchy from 40,000 ft.
load/store FUs
retire stations
eI$0
fI$0
D$1
eI$1
L$2
Harvard level 1
shared level 2
TLB
DRAM
ROM
MMIO
device controllers
devices
dPLB
iPLB
fI$1
virtual addresses
physical addresses
The Mill uses virtual caching and the single address space model.

## Slide 51
Memory model
Mill:
All tasks use the same virtual addresses, no aliasing or translation across tasks or OS.
Program addresses must be translated to physical addresses before being looked up in cache.
Traditional
bottleneck
load
operation
translation/
protection
lines
regs
fault
virtual
address
physical
address
cache
CPU
TLB
data
load
operation
protection
lines
belt
fault
PLB
CPU
cache
data
virtual
address

## Slide 52
Why put translation in front of the cache?
bottleneck
load
operation
translation/
protection
lines
regs
fault
virtual
address
physical
address
cache
CPU
TLB
data
Different programs must overlap addresses (aliasing) to fit in 32-bit memory. Translation gives each program private memory, even while using the same bit patterns as pointers.
The cost:
  On the critical path, TLBs must be very fast, small, and power-hungry, and frequently multilevel. Big programs can see 20% or more TLB overhead.
Traditional

## Slide 53
Why put translation after the cache?
Mill:
All tasks use the same virtual addresses, no aliasing or translation across tasks or OS.
load
operation
protection
lines
belt
fault
PLB
CPU
cache
data
virtual
address
TLB out of critical path, only referenced on cache misses and evicts; can be big, single-level, and low power.
Pointers can be passed to OS or other tasks without translation; simplifies sharing and protection for apps.
Protection checking done in parallel with cache access.

## Slide 54
Memory allocation - conventional
Operating systems on conventional hardware do not actually allocate memory when the program allocates address space.
mmap(0,1000000,,,);
OS page table
PTE
PTE
PTE
PTE
PTE
PTE
PTE
PTE
x 256
The entries identify the page as unrealized.
The first time the address is touched, the hardware looks up the PTE, finds the page is unrealized, and traps.
store(,,)
TRAP!
The OS allocates a physical page, zeroes it, and fixes up the PTE. This all takes a long time.

## Slide 55
Memory allocation - Mill
Operating systems on the Mill do not create PTEs when allocating address space. All address space not covered by a PTE is unrealized by default.
mmap(0,1000000,,,);
OS page table
Reads and writes that are satisfied in cache do not search for a PTE.
store(,,)
There is no associated physical memory. The address space is backless.
PTE
PTE
PTE
PTE
other PTEs

## Slide 56
A Mill backless load miss
load/store FUs
D$1
D$2
TLB
dPLB
OS page table
PTE
PTE
PTE
PTE
Issue load
Check access permissions –
Check d$1 –
Check d$2 –
Find PTE –
Return a zero
OK
nope
nope
none
retire station
0
No DRAM!
DRAM

## Slide 57
A Mill backless evict
load/store FUs
D$1
D$2
TLB
dPLB
DRAM
OS page table
PTE
PTE
PTE
PTE
Cache contention can force eviction of lines from cache to memory.
Select LRU line
Search for PTE –
Allocate physical page
Update page table
Copy data to memory
Discard cache line
none
PTE
All steps in hardware
No traps to OS!

## Slide 58
The fine print
The OS page table and the TLB support pages of multiple sizes, including one line.
The hardware allocates one-line pages for evicts from a pool represented as a bit mask over a contiguous block. Running out of one-line pages causes the hardware to choose another block from a pool of blocks. Running low on blocks triggers a trap.
A background OS process allocates blocks for the block pool for the hardware to use, and consolidates small physical pages that are nearby in virtual space into larger physical pages that are zero-filled.

## Slide 59
When stores are unnecessary
implicit zero

## Slide 60
Problem: transient stack frames
The largest fraction of memory references are to the local stack frame. Many of those references are initialization, frequently to zero.
When a stack frame exits, nearly all the lines in the frame will be dirty and will be written back to DRAM. The write-back is pointless because the lines are dead.
Reading uninitialized data is a common bug.
Reading the stack rubble of previously called functions is a common path for security exploits.

## Slide 61
Implicit zero
SP
data stack
IZ
The IZ special register holds a bit map of the cache lines at the top of the data stack.
The stackf operation allocates a frame in the data stack, in units of cache lines.
stackf(4)

## Slide 62
Implicit zero
SP
data stack
IZ
A load from a implicitly-zero line returns a zero without going to the memory hierarchy.
load(fp+100,b,)
retire station
request
0

## Slide 63
Implicit zero
SP
data stack
IZ
A store to a implicitly-zero writes its data, sets the rest of the line to zero, and clears the IZ bit.
store(fp+100,<data>)
request

## Slide 64
Implicit zero
SP
data stack
IZ
A store to a implicitly-zero writes its data, sets the rest of the line to zero, and clears the IZ bit.
store(fp+100,<data>)
request
This is called realizing the implicitly-zero line.

## Slide 65
Implicit zero
SP
data stack
IZ
A return operation discards any realized lines in the cache, unwinds the stack frame, and clears the IZ bits.
return()
Realized lines are discarded. They will not be written back to DRAM.

## Slide 66
The fine print #1
Compiler optimization can remove zero-initialization operations that are obviated by the IZ.
Uninitialized-data detecting tools such as valgrind and Purify must be aware of the existence of IZ in their operation and analysis.
While the IZ machinery could in principle be used for other memory allocation, the Mill does not at present do so.
The IZ covers the top of stack; it may cover lines belong to several different frames.

## Slide 67
The fine print #2
A stackf frame allocation may be bigger than the IZ mask register can cover. Excess lines are realized to zero in cache as part of the allocation. Code can force realization of the IZ by calling a function that allocates a frame larger than the IZ.
Task switch realizes all implicitly-zero lines.
Each IZ is private to the executing core. In a multicore the member implementation may elect to realize a implicitly-zero line that has its address taken; may realize the entire IZ if any line has its address taken; or may explicitly realize an object iff a taken address might leak to another core.

## Slide 68
When cores collide
sequential consistency

## Slide 69
Memory consistency
program:
…
op1
op2
load1
op3
store1
op4
load2
op5
…
semantic order
load
load
store
semantic order
instruction:

## Slide 70
program:
…
op1
op2
load1
op3
store1
op4
load2
op5
…
semantic order
Memory consistency
load1
load2
store1
semantic order
instruction:

## Slide 71
Memory consistency
load1
load2
store1
instruction:
semantic order
function units:
loadFU
storeFU
loadFU
load1
load2
store1

## Slide 72
Memory consistency
load1
load2
store1
instruction:
function units:
loadFU
storeFU
loadFU
requests:
D$1

## Slide 73
function units:
Memory consistency
loadFU
storeFU
loadFU
requests:
D$1
store1
load2
load1
D$2
DRAM

## Slide 74
Sequential consistency
source code
instructions
functional units
requests
data
No overtaking!
Monocore sequential consistency
No membar instructions
No memory race bugs
Mill cache coherence protocol preserves sequential consistency in on-chip multicore configurations, while cutting CC overhead in half.
Multicore is the subject of a future talk in this series.
Sign up at ootbcomp.com/mailing-list for invites.

## Slide 75
The summary #1
The Mill:
Is immune to false aliasing
Can hide load latency and cache miss
Performance like out-of-order hardware
Cost like static scheduling software
Loads reflect memory as-of load retire
Implicitly prefetches across function calls
The compiler knows when ops retire

## Slide 76
The summary #2
The Mill:
Doesn’t write back dead frames
Doesn’t need to zero-initialize stack frames
Substantial saving in general-purpose code
No pointless writes
Prevents uninitialized-frame bugs
Frame data is always initialized

## Slide 77
The summary #3
The Mill:
Eliminates 90%+ of TLB references
Has no store buffers
Stores go to cache immediately
Large power and latency saving
Shared address space simplifies OS
No pointer translation needed.

## Slide 78
The summary #4
The Mill:
Uniform sequential consistency throughout
Backless data needs no physical pages
No page allocation overhead
No OS involvement
No membar instructions
No memory race bugs

## Slide 79
Want more?
Sign up for technical announcements, white papers, etc.:
ootbcomp.com