## Slide 1
Number five of a series
Drinking from the Firehose
More work from less code
in the Mill™ CPU Architecture

## Slide 2
The Mill CPU
The Mill is a new general-purpose commercial CPU family.
The Mill has a 10x single-thread power/performance gain over conventional out-of-order superscalar architectures, yet runs the same programs, without rewrite.
This talk will explain:
templated (generic) encoding
how to deal with error events in speculated code
implicit state in floating-point
vectorization of while-loops

## Slide 3
Talks in this series
Encoding
The Belt
Memory
Prediction
Metadata and speculation
Specification
Execution
…
You are here
Slides and videos of other talks are at:
ootbcomp.com/docs

## Slide 4
addsx(b2, b5)
The Mill Architecture
Metadata and speculation
New with the Mill:
Width and scalarity polymorphism
Compact, regular instruction set
Speculative data
No exception-carried dependencies
Missing data
Missing is not the same as wrong
Vector while loops
Searches at vector speed
Floating-point metadata
Data-carried floating point state

## Slide 5
Caution!
Gross over-simplification!
This talk tries to convey an intuitive understanding to the non-specialist.
The reality is more complicated.
(we try not to over-simplify, but sometimes…)

## Slide 6
80% of code is in loops
Pipelined loops have unbounded ILP
  DSP loops are software-pipelined
But –
  few general-purpose loops can be piped
  (at least on conventional architectures)
Solution:
  pipeline (almost) all loops
  throw function hardware at pipe
Result: loops now < 15% of cycles
33 operations per cycle peak ??? Why?
Not quite right

## Slide 7
and vectorize
^
or vectorized
^
80% of code is in loops
Pipelined loops have unbounded ILP
  DSP loops are software-pipelined
But –
  few general-purpose loops can be piped
  (at least on conventional architectures)
Solution:
  pipeline (almost) all loops
  throw function hardware at pipe
Result: loops now < 15% of cycles
Much better!
33 operations per cycle peak ??? Why?

## Slide 8
A quote:
“I'd love to see it do well, I have a vested interest doing audio/DSP and this thing eats loops like goats eat underwear.”
TheQuietestOne, on Reddit.

## Slide 9
Why emphasize vectorization?
vectorization is SIMD – single operations working on multiple data elements in parallel
pipelining is MIMD – multiple operations each working on its own data, but arranged for lower overhead
Both are easy to use for simple fixed-length loops without control flow, and impossible (on conventional machines) for even simple while-loops. This talk explains how the Mill vectorizes loops containing complex control flow.
Software pipelining is the subject of a future talk.
Vectorization is not the same as software pipelining. They are both ways to make loops more efficient, but:

## Slide 10
Self-describing data
metadata
Metadata is data about data.

## Slide 11
Metadata
In the Mill core, each data element is in internal format and is tagged by the hardware with extra metadata bits.
12345678
data
meta
data element
A belt or scratchpad operand can be a single scalar element

## Slide 12
Internal format
Each Mill data element in internal format is tagged by the hardware with extra metadata bits.
12345678
data
meta
data element
A belt or scratchpad operand can be a single scalar element.
element
meta
12345678
scalar operand
12345678
data
meta
The operand has metadata too.

## Slide 13
Scalar and vector operands
There is metadata for the operand as a whole too.
12345678
data
meta
data element
A belt or scratchpad operand can also be a vector of elements, all of the same size and each with metadata.
meta
12345678
12345678
data
meta
12345678
12345678
12345678
12345678
data
meta
12345678
data
meta
12345678
data
meta
vector operand

## Slide 14
External interchange format
Data on the belt and in the scratchpad is in internal format. Data in the caches and DRAM is in external interchange format and has no metadata.
A load adds metadata to loaded values:
D$1
load(,,)
0x5c
0x5c
representation in core
representation in memory

## Slide 15
Width and scalarity
A metadata tag attached to each Mill operand gives the byte width of the data elements. Supported widths are scalars of 1, 2, 4, 8, and 16 bytes.
Tag metadata also tells whether the operand is a single scalar or a fixed-length vector of data, with all elements of the same scalar width. Vector size varies by member.
tag
tag
Load operations set the width tag as loaded.

## Slide 16
…
…
0x5c
External interchange format
Data on the belt and in the scratchpad is in internal format. Data in the caches and DRAM is in external interchange format and has no metadata.
Stores strip metadata from stored values:
D$1
store(,)
…
0x5c
Stores use the metadata width to size the store.

## Slide 17
Numeric Data Sizes
integer
8, 16, 32, 64, 128
pointer
64
IEEE binary float
16, 32, 64, 128
IEEE decimal
32, 64, 128
ISO C fraction
8, 16, 32, 64, 128
Underlined widths are optional, present in hardware only in Mill family members intended for certain markets and otherwise emulated in software

## Slide 18
Scalar vs. Vector operation - SIMD
+
Vector operation – all
elements in parallel
Scalar operation –
only low element
The Mill operation set is uniform – all ops work either way.
15
17
3
17
16
2
15
12
3
+
20
22
12
0
4
20

## Slide 19
Width and Scalarity Polymorphism
+
One opcode performs all these operations, based on the metadata tags. Unused bits are not driven, saving power.
add

## Slide 20
However, compiler code generation is simpler with width tagging because the back ends do not have to code-select for differences in width. The generated code is also more compact because it doesn't carry width info.
Type information is maintained by the compilers for the types defined by each language, which are too varied for direct hardware representation. Language type distinctions reach the hardware via the opcodes in the instructions, not the data tags.
Width vs. type
Width metadata tags tell how big an operand is, not what type it is:
173923355
3.14159
4-byte int
4-byte float
same tag

## Slide 21
When it doesn’t fit…
The widen operation doubles the width.
The narrow operation halves the width.
widen
narrow
widen
narrow
Vector widen yields two result vectors of double-width elements

## Slide 22
Go both ways…
speculation
Speculation is doing something before you know you must

## Slide 23
What to do with idle hardware
if (a*b == c) { f(x*3); } else { f(x*5); }
(everything in the core already)
mul a, b
eql <a*b>, c
brfl <a*b == c>, lab
mul x, 3
call f, <x*3>
lab:
  mul x, 5
  call f, <x*5>
timing:
3
1
1
3
1
9
mul a, b; mul x, 3; mul x, 5
eql <a*b>, c
brfl <a*b == c>, lab
call f, <x*3>
lab:
  call f, <x*5>
3
1
1
1
6
Speculation is the triumph of hope over power consumption

## Slide 24
Speculative floating point
metafloat

## Slide 25
Floating point flags
The IEEE754 floating point standard defines five flags that are implicit output arguments of floating point operations. Exception conditions set the flags.
x = y + z
y
z
y+z
divide by zero
inexact
invalid
underflow
overflow
+
On a conventional machine, the operation updates a global floating-point state register.
The global state prevents speculation!
d
x
v
o
u
global state

## Slide 26
Floating point flags
The IEEE754 floating point standard defines five flags that are implicit output arguments of floating point operations.
x = y + z
+
divide by zero
inexact
invalid
underflow
overflow

## Slide 27
Floating point flags
The IEEE754 floating point standard defines five flags that are implicit output arguments of floating point operations.
x = y + z
+
divide by zero
inexact
invalid
underflow
overflow
d
x
v
o
u
z
y
y+z

## Slide 28
Floating point flags
The IEEE754 floating point standard defines five flags that are implicit output arguments of floating point operations.
x = y + z
+
divide by zero
inexact
invalid
underflow
overflow
d
x
v
o
u
y+z
On a Mill, flags become metadata in the result.

## Slide 29
d
x
v
o
u
y+z
0
1
0
0
0
y+z
Floating point flags
The meta-flags flow though subsequent operations.
0
1
0
0
1
w*x

## Slide 30
0
1
0
0
1
0
1
0
0
1
0
1
0
0
0
0
1
0
0
0
y+z
Floating point flags
The meta-flags flow though subsequent operations.
w*x
+
OR
y+z+w*x
0
1
0
0
1
add
y+z
w*x

## Slide 31
0
1
0
0
0
y+z
Floating point flags
The meta-flags flow though subsequent operations.
0
0
0
0
1
w*x
+
OR
y+z+w*x
0
1
0
0
1
add
store
y+z+w*x
memory
fpState register
0
0
0
0
0
0
1
0
0
1
OR
The meta-flags have been realized.

## Slide 32
Choose one…
pick

## Slide 33
The pick operation
pick selects one of two source operands from the belt, based on the value of a third control operand.
pick has zero latency; it takes place entirely within belt transit. No data is actually moved in pick; only the belt routing to consumers changes.
12
12
1
?
:
3

## Slide 34
Vector pick
3
17
16
2
12
0
4
20
0
?
:
12
0
4
20
A scalar selector chooses between complete vectors.

## Slide 35
Vector pick
3
17
16
2
12
0
4
20
?
:
12
0
4
20
A vector selector chooses between individual elements.
12
20
17
16
0
1
1
0

## Slide 36
mul a, b; mul x, 3; mul x, 5
eql <a*b>, c
brfl <a*b == c>, lab
call f, <x*3>
lab:
  call f, <x*5>
3
1
1
1
6
What to do with idle hardware (improved)
if (a*b == c) { f(x*3); } else { f(x*5); }

## Slide 37
mul a, b; mul x, 3; mul x, 5
eql <a*b>, c
brfl <a*b == c>, lab
call f, <x*3>
lab:
  call f, <x*5>
3
1
1
1
6
What to do with idle hardware (improved)
if (a*b == c) { f(x*3); } else { f(x*5); }
f(a*b == c ? x*3 : x*5);
mul a, b; mul x, 3; mul x, 5
eql <a*b>, c
pick <a*b == c>, <x*3>, <x*5>
call f, <a*b == c ? x*3 : x*5>
3
1
0
1
5
And the branch is gone!
ternary if
if-conversion

## Slide 38
Why is removing the branch important?
f(a*b == c ? x*3 : x*5);
mul a, b; mul x, 3; mul x, 5
eql <a*b>, c
pick <a*b == c>, <x*3>, <x*5>
call f, <a*b == c ? x*3 : x*5>
3
1
0
1
5
And the branch is gone!
For more explanation see:
ootbcomp.com/docs/prediction
Branches occupy predictor table space, and may cause stalls if mispredicted.

## Slide 39
f(a*b == c ? x*3 : x*5);
mul a, b; mul x, 3; mul x, 5
eql <a*b>, c
pick <a*b == c>, <x*3>, <x*5>
call f, <a*b == c ? x*3 : x*5>
3
1
0
1
5
For more explanation see:
ootbcomp.com/docs/belt
pick does not move any data. It alters the belt renaming that takes place at every cycle boundary.
pick
0
How does pick take zero cycles?

## Slide 40
When data is invalid…
NaR

## Slide 41
x = b ? *p : *q;
load *p; load *q;
pick b : <*p> : <*q>
store x, <b?*p:*q>
Loading both *p and *q is speculative; one is unnecessary,
but we don’t know which one.
What if p or q are null pointers?
Oops!
The null load would fault, even if not used.
What if speculation gets in trouble?

## Slide 42
Every data element has a NaR (Not A Result) bit in the element metadata. The bit is set whenever a detected error precludes producing a valid value.
value
OK
oops
payload
kind
where
error kind
failing operation location
operation
A debugger displays the fault detection point.
NaR bits

## Slide 43
A speculable operation has no side-effects and propagates NaRs through both scalar- and vector operations.
Speculable:
load, add, shift, pick, …
A non-speculable operation has side-effects and faults on a NaR argument.
Non-speculable:
store, branch, …
FAULT!
(Non-)speculable operations

## Slide 44
x = b ? *p : *q;
load *p;
load *q;
pick b ? *p : *q
belt
null
q
0x?
p
true
b
42
*p
NaR
*q
42
pick
What if speculation gets in trouble?

## Slide 45
x = b ? *p : *q;
load *p;
load *q;
pick b ? *p : *q
store x, <b?*p:*q>
belt
null
q
0x?
p
true
b
42
*p
NaR
*q
42
pick
42
pick
memory
What if speculation gets in trouble?

## Slide 46
x = b ? *p : *q;
load *p;
load *q;
pick b : *p : *q
store x, <b?*p:*q>
belt
null
q
0x?
p
true
b
42
*p
NaR
*q
NaR
pick
memory
false
b
X
Mill speculation is error-safe
FAULT!
What if speculation gets in trouble?

## Slide 47
Integer overflow
254
3
+
unsigned integer add
addu
addux
addus
adduw
1
NaR
255
257
truncated byte result
eventual exception
saturated byte result
double-width full result
All operations that can overflow offer the same four alternatives
Example has byte width, but applies to any scalar or vector element width.
(1-byte data)

## Slide 48
Augmented types
Mill standard compilers augment the host languages with new types, supported in hardware.
__saturating short greenIntensity;
Saturating arithmetic replaces overflowed integer results with the largest possible value, instead of wrapping the result. It is common in signal processing and video.
__excepting int boundedValue;
Excepting arithmetic replaces overflows with a NaR, leading eventually to a hardware exception. This precludes many exploits (and bugs) that depend on programs silently ignoring overflow conditions.

## Slide 49
Missing values
None

## Slide 50
Wrong? or just missing?
A NaR is bad data, while a None is missing data.
if (a<0) x = y;
lss a, 0
brfl <eql>, join
store x, y
br join
join:
x = a<0 ? y : None;
lss a, 0
pick <eql>, y, None
store x, <pick>
Both NaR and None flow through speculation.
Non-speculative operations fault a NaR, but do nothing at all for a None.
if-convert to:

## Slide 51
‘None’ behavior
“None” values propagate through computation like a NaRs, but are simply discarded by state-changing operations like store.
Source code:
if (a<0) x = y;
a
<0
7
17
false
5
None
None
Nothing happens –
‘x’ is unchanged
?:
y
x
memory

## Slide 52
Boolean reduction
smear

## Slide 53
Boolean reduction
The smear operation copies vectors of bool
It copies the first true element into subsequent elements.
0
0
1
1
0
1
0
1
1
1
1
1
smeari copies directly, element by element.
1
1
0
0

## Slide 54
0
0
1
1
0
1
0
1
1
1
1
1
1
smeari copies directly, element by element.
0
0
1
1
1
1
1
1
Boolean reduction
The smear operation copies vectors of bool
It copies the first true element into subsequent elements.
0
0
1
1
0
1
0
1
smearx offsets copy by one position
and returns the offset value as a second result
0
1
0
0

## Slide 55
Vectorizing while-loops
strcpy
strcpy is a convenient example – it is well known and fits on a slide. It is not a special case.
The technique shown works for arbitrary internal control flow.

## Slide 56
char c; do { *dest++ = c = *src++; } while (c != 0);
char* strcpy(char* dest, const char* src)
load *src, bv
ˈhˈ
ˈeˈ
ˈlˈ
ˈlˈ
ˈoˈ
ˈsˈ
0
0
memory
increasing addresses

## Slide 57
0
0
0
0
0
0
1
1
char c; do { *dest++ = c = *src++; } while (c != 0);
char* strcpy(char* dest, const char* src)
load *src, bv
eql <load>,0
ˈhˈ
ˈeˈ
ˈlˈ
ˈlˈ
ˈoˈ
ˈsˈ
0
0
load
equal zero

## Slide 58
char c; do { *dest++ = c = *src++; } while (c != 0);
char* strcpy(char* dest, const char* src)
eql <load>,0
smearx <eql>
ˈhˈ
ˈeˈ
ˈlˈ
ˈlˈ
ˈoˈ
ˈsˈ
0
0
0
0
0
0
0
0
1
1
load
eql 0
smearx
0
0
0
0
0
1
0
1
1

## Slide 59
ˈhˈ
ˈeˈ
ˈlˈ
ˈlˈ
ˈoˈ
ˈsˈ
0
0
load
ˈhˈ
ˈeˈ
ˈlˈ
ˈlˈ
ˈoˈ
ˈsˈ
0
0
char c; do { *dest++ = c = *src++; } while (c != 0);
char* strcpy(char* dest, const char* src)
0
0
0
0
0
0
1
1
eql 0
0
0
0
0
0
1
0
1
1
smearx
smearx <eql>
pick <smearx0>,None,<load>
None
None
None
None
None
None
None
None
?
:
pick

## Slide 60
ˈhˈ
ˈeˈ
ˈlˈ
ˈlˈ
ˈoˈ
ˈsˈ
0
0
None
None
None
None
None
None
None
None
None
char c; do { *dest++ = c = *src++; } while (c != 0);
char* strcpy(char* dest, const char* src)
0
0
0
0
0
0
1
1
eql 0
0
0
0
0
0
1
0
1
1
smearx
smearx <eql>
pick <smearx0>,None,<load>
pick
?
:
ˈhˈ
ˈeˈ
ˈlˈ
ˈlˈ
ˈoˈ
ˈsˈ
0
0
load
ˈhˈ
ˈeˈ
ˈlˈ
ˈlˈ
ˈoˈ
None
0

## Slide 61
ˈhˈ
ˈeˈ
ˈlˈ
ˈlˈ
ˈoˈ
None
0
None
ˈhˈ
ˈeˈ
ˈlˈ
ˈlˈ
ˈoˈ
ˈsˈ
0
0
char c; do { *dest++ = c = *src++; } while (c != 0);
char* strcpy(char* dest, const char* src)
0
0
0
0
0
0
1
1
eql 0
0
0
0
0
0
1
0
1
1
smearx
pick <smearx0>,None,<load>
store *dest, <pick>
pick
None
None
None
None
None
None
None
None
?
:
ˈhˈ
ˈeˈ
ˈlˈ
ˈlˈ
ˈoˈ
ˈsˈ
0
0
load
to memory
store
ˈhˈ
ˈeˈ
ˈlˈ
ˈlˈ
ˈoˈ
0

## Slide 62
1
0
0
0
0
0
1
0
1
smearx
ˈhˈ
ˈeˈ
ˈlˈ
ˈlˈ
ˈoˈ
None
0
None
ˈhˈ
ˈeˈ
ˈlˈ
ˈlˈ
ˈoˈ
ˈsˈ
0
0
char c; do { *dest++ = c = *src++; } while (c != 0);
char* strcpy(char* dest, const char* src)
0
0
0
0
0
0
1
1
eql 0
store *dest, <pick>
brfl smearx1, loop
pick
None
None
None
None
None
None
None
None
?
:
ˈhˈ
ˈeˈ
ˈlˈ
ˈlˈ
ˈoˈ
ˈsˈ
0
0
load
to memory
branch if false
1
loop exited
(not taken)

## Slide 63
ˈhˈ
ˈeˈ
ˈlˈ
ˈlˈ
ˈoˈ
0
None
None
1
0
0
0
0
0
1
0
1
smearx
0
ˈhˈ
ˈeˈ
ˈlˈ
ˈlˈ
ˈoˈ
ˈsˈ
0
char c; do { *dest++ = c = *src++; } while (c != 0);
char* strcpy(char* dest, const char* src)
0
0
0
0
0
0
1
1
eql 0
pick
None
None
None
None
None
None
None
None
?
:
ˈhˈ
ˈeˈ
ˈlˈ
ˈlˈ
ˈoˈ
ˈsˈ
0
0
load
to memory
1
What if the null is on the edge?
ˈeˈ
0
0
0
ˈeˈ
ˈsˈ
0
ˈeˈ
branch if false
loop exited
(not taken)
ˈhˈ
ˈeˈ
ˈlˈ
ˈlˈ
ˈoˈ
ˈeˈ
0
ˈsˈ

## Slide 64
Protection trouble
What if the load violates protection boundaries?
memory
protected
accessible
load *p, bv
load request
ˈfˈ
ˈoˈ
ˈoˈ
0
ˈxˈ
NaR
NaR
NaR

## Slide 65
Protection trouble
What if the load violates protection boundaries?
memory
protected
acccessible
load *p, bv
ˈfˈ
ˈoˈ
ˈoˈ
0
ˈxˈ
NaR
NaR
NaR
0
0
0
1
0
NaR
NaR
NaR
eql <load>, 0
smearx <eql>
0
0
0
0
1
1
1
1
pick smearx,None,load
ˈfˈ
ˈoˈ
ˈoˈ
0
None
None
None
None
store <pick>
ˈfˈ
ˈoˈ
ˈoˈ
0
memory

## Slide 66
Protection trouble
What if the load violates protection boundaries?
memory
protected
acccessible
load *p, bv
ˈfˈ
ˈoˈ
ˈoˈ
ˈxˈ
ˈxˈ
NaR
NaR
NaR
0
0
0
0
0
NaR
NaR
NaR
eql <load>, 0
smearx <eql>
0
0
0
0
0
0
NaR
NaR
pick smearx,None,load
store <pick>
ˈfˈ
ˈoˈ
ˈoˈ
ˈxˈ
ˈxˈ
NaR
NaR
NaR
FAULT!

## Slide 67
strcpy code
Mill phasing merges consecutive dependent operations into a single instruction. Mill software pipelining merges instructions in a loop into fewer instructions. The operations are the same as without phasing or pipelining, but organized differently in time.
The strcpy copies one vector-full of characters per iteration, 8 per iteration on Tin, 32 per iteration on Gold. The kernel fits in three phased instructions on a large enough Mill, and only one when pipelined.
Phasing and pipelining are subjects of upcoming talks.
Sign up for talk announcements at:
ootbcomp.com/mailing-list

## Slide 68: Loop control – vector remaining
1
0
0
0
1
1
1
1
1
remaining b5, bv
Count-loops exit after a fixed number of iterations (which may not end on a vector boundary) rather than on a predicate like while-loops.
3
A width argument tells the desired vector element width.
A count argument tells the remaining number of iterations.
A result is a bool vector mask with count leading false.
remaining is used like smear to hide after-exit effects.
A second result is an exit flag

## Slide 69: Loop control – vector remaining
0
0
0
1
0
1
0
1
remaining b5
The remaining operation also can take a bool vector mask, and return a count of the number of false values up to the first true, which represents the number of iterations up to the exit point.
The scalar and vector remaining ops are inverses of each other, converting from count to mask and vice versa.
The smear and remaining ops support vectorizing loops that do not end on a vector boundary. Many “search” loops need also to know how far they got before the exit condition was satisfied.
3

## Slide 70: Vector remaining example: strlen()
strlen
inner loop:
'\0'
'a'
'b'
'c'
'd'
'\0'
'e'
'f'
1
0
0
0
0
1
0
0
1
3
eql
any
remaining
repeat if false
(from mem)
len
add
again: load <src>,bv; eql <load>,0; add src,8;
remaining <eql>; add <len>, <remaining>
any <remaining>; brfl <any>, again;
load

## Slide 71
Summary #1:
The Mill:
Has vector forms for all meaningful ops
Tracks operand size and scalarity
Operations are generic; 7x fewer opcodes
Regular ISA makes compiler easier
Can speculate through errors
Reports error location on fault

## Slide 72
Summary #2
The Mill:
Distinguishes missing data
Can load across protection boundaries
Valid data is usable; invalid data cannot be seen
Automatically avoids side effects
Detects integer overflow
Saturation, exception, and wraparound supported

## Slide 73
Summary #3
The Mill:
Can speculate floating-point operations
Can vectorize “while” loops
And conditional exits in general
Floating-point exception flags reported correctly
Can vectorize uneven counting loops
And determine “while” counts

## Slide 74
Shameless plug
For technical info about the Mill CPU architecture:
ootbcomp.com/docs
To sign up for future announcements, white papers etc.
ootbcomp.com/mailing-list