## Slide 1
One of a series…
Drinking from the Firehose
Switches: a Mill story

## Slide 2
Encoding
The Belt
Memory
Prediction
Metadata
Execution
Security
Specification
Pipelining
Compiling
Switches
…
You are here
Slides and videos of other talks are at:
MillComputing.com/docs
Talks in this series
…

## Slide 3
Caution!
Gross over-simplification!
This talk tries to convey an intuitive understanding to the non-specialist.
The reality is more complicated.
(we try not to over-simplify, but sometimes…)

## Slide 4
Talk purpose
Most of our talks are about new architectural ideas in the Mill…
Not this one
This is about how architecture impacts “good code”
We’ll be using the “switch” statement as a very small example:
switch (val) {
case thisVal: doThis(); break;
case thatVal: doThat(); break;
default: doOther(); break;
}

## Slide 5
Does switch performance make a difference?
In some cases, yes:
  Lexers
  Byte-code interpreters
  Network dispatch
  …
In most cases, not very but …
Many a mickle makes a muckle.
Robert Burns

## Slide 6
Why switches?
Happenstance:
  A question on comp.arch asked:
    “Does the Mill have any special ops to handle switches?”
  Answer: no (and why)
  A question on Mill Forum asked:
    “Read answer, didn’t understand, here’s an example, explain”
  Crash compiler 
  Fix compiler 
  Pretty good code, good example, post to Forum
Yes, Virginia, there still are newsgroups
millcomputing.com/forum/the-mill/
Tool chain pre-Alpha

## Slide 7
The example
int bar(int x) {
  switch(x) {
  case 0: return 1;
  case 2:
  case 3: return foo(x);
  case 5: return 5;
  case 6: return 6;
  case 7: return 7;
  case 100: break;
  default: return 4; }
return 3; }
(Thanks to Forum reader @Goldbug)

## Slide 8
Terminology
int bar(int x) {
  switch(x) {
  case 0: return 1;
  case 2:
  case 3: return foo(x);
  case 5: return 5;
  case 6: return 6;
  case 7: return 7;
  case 100: break;
  default: return 4; }
return 3; }
the selector
a case
a target
a case run

## Slide 9
Switch implementation
x == 0
x == 2
x == 3
x == 5
x == 6
x == 7
x == 100
Linear chain of if’s
Entry per non-default case
Average ½ tests executed
Profile optimization: test common cases first
Good when very few cases
(preferably one)

## Slide 10
Switch implementation
Binary tree of if’s
Entry per case run
LogN tests executed
x < 8
∞
x < 100
8-99
100
-∞
x < 4
x < 1
x < 0
x < 2
x < 5
0
1
2-3
4
5
x < 7
6
7
x < 6
x < 101
Exercise: when is N/2 < logN?

## Slide 11
Switch implementation
x < 0
∞
-∞
x < 101
0
1
2
3
4
5
6
7
8
9
10
11
98
99
100
Jump table
Entry per case, not per case run
Two tests plus indexed indirect jump
Where do you put the table?
  In the code?
  In the data space?

## Slide 12
Why are switches annoying?
Megamorphic:
  Wide distribution of likely taken paths
  Rare to always go the same way – even with good history
Yes, this happens, but rare in the wild
“But I can rewrite this as
  if (x == hotval) {} else switch(x){}”
Yes you can – but you still have a multiway branch
All you’ve done is hand-compile it
This talk is about the impact of architecture on switches –
It is not about how best to write one

## Slide 13
Why are switches annoying?
Megamorphic:
  Wide distribution of likely taken paths
  Modal path has low probability
Most path distributions look like this
(plus some never-taken paths not shown)
Your predictor will guess the modal path every time
Unless the modal path is taken 90+% of the time
Welcome to mispredict hell!
To a first approximation, a switch will mispredict
EVERY TIME!

## Slide 14
test low
test high
load address
jump
Why are switches annoying?
x < 0
∞
-∞
x < 101
0
1
2
3
4
5
6
7
8
9
10
11
98
99
100
Jump table
Entry per case, not per case run
Two tests plus indexed indirect jump
Predict OK
Mispredict

## Slide 15
Why are switches annoying?
x < 0
∞
-∞
x < 101
0
1
2
3
4
5
6
7
8
9
10
11
98
99
100
Jump table
Entry per case, not per case run
Two tests plus indexed indirect jump
test low
test high
load address
TLB miss
D$1 miss
mispredict
jump

## Slide 16
Why are switches annoying?
x < 0
∞
-∞
x < 101
0
1
2
3
4
5
6
7
8
9
10
11
98
99
100
Jump table
test low
test high
load address
TLB miss
D$1 miss
jump
mispredict
- why not put it in the code space, after the jump?
Table is read-only, like code
No TLB miss
No i$1 miss
Special range-check instruction?

## Slide 17
Welcome to architecture
Jump table - why not put it in the code after the jump?
Table-in-code works for machines with no cache and data paths <= address size.
Today’s machines have caches that fill line-at-a-time, and instruction fetch 16(+ or ++) bytes at a time.
Where do you put the shifters that select one address out of the middle of a code line? In a critical path for clock?
You don’t. Your microcode loads the line to the data side, where the shifters already exist. Live with it.
Say - 1980.

## Slide 18
Branch prediction
To a first approximation, a switch will mis-predict
EVERY TIME!
x == 0
x == 2
x == 3
x == 5
x == 6
x == 7
x == 100
First taken
predicted
actual
Mispredict when execute == 5
Toss pipeline, in-flights, re-orders; restore state; resume decode
~15-20 cycles typical
The cost of the search chain disappears into the cost of the miss
This is early-miss: the miss precedes the prediction
The good news: only one miss 
F
F
F
F
F
T
T
(will miss)

## Slide 19
Why are switches annoying?
To a first approximation, a switch will mis-predict
EVERY TIME!
x == 0
x == 2
x == 3
x == 5
x == 6
x == 7
x == 100
predicted
actual
Mispredict when execute == 5
Execute == 6, miss again
~30-40 cycles
May miss again on actual
This is late-miss: the prediction precedes the miss
The bad news: many misses 
second guess
F
F
T
F
T
F
T

## Slide 20
Switch implementation
x == 0
x == 2
x == 3
x == 5
x == 6
x == 7
x == 100
Linear chain of if’s
Average ½ tests executed
Miss once if you’re lucky
Potentially miss several times

## Slide 21
Switch implementation
Binary tree of if’s
LogN tests executed
x < 4
x < 1
x < 0
x < 8
x < 2
x < 5
∞
-∞
0
1
2/3
4
5
x < 7
6
7
x < 100
8/99
100
x < 6
x < 101
Exercise: for a given selector distribution, what is the expected miss rate?
Answer: to a first approximation, miss at every other level

## Slide 22
In short:
YUCK!

## Slide 23
Architecture
What does the Mill bring to the switch party?
  Wide issue: 5-30+ ops per cycle superscalar
  Phasing: schedule short dataflows, not single ops
  Exit prediction: not branch prediction
  5 cycle mispredict: not 20+
  Multi-branching: several branch ops in one instruction

## Slide 24
Specification
abstract
Mill CPU architecture
family members
Tin
Copper
Silver
Gold
The Mill is a family of member CPUs sharing an abstract operation set and micro-architecture.
specification driven
Members differ in concrete operation set and micro-architecture..
A designer describes a concrete member by writing a specification.

## Slide 25
Specification
abstract
Mill CPU architecture
family members
Tin
Silver
Gold
tools
compiler
asm
debugger
HWgen
sim
Toolchain software automatically creates system software, verification tests, documentation, and a hardware framework for the new member from the specification.
specification driven
Copper
data driven

## Slide 26
The target: Silver
This talk will use Silver, a mid-range Mill
  32k d$1, 2x 1k i$0, 2x 64k i$1 – plus other caches outside the core
  4x ALU, 2x FPU, 3x branch, 4x LS, 9x misc – not all at once
  Maximum sustained issue/retire rate 17 ops per clock
  You can think of Silver as a 17-wide superscalar
Yes, that is a mid-range Mill

## Slide 27
The example
int bar(int x) {
  switch(x) {
  case 0: return 1;
  case 2:
  case 3: return foo(x);
  case 5: return 5;
  case 6: return 6;
  case 7: return 7;
  case 100: break;
  default: return 4; }
return 3; }
(remember this?)

## Slide 28
The genAsm
define external function @bar w (in w) {
label $0:
%1 = con(w(1));
switch(%0, $1, 0, $2, 2, $3, 3, $3, 5, $4, 6, $5, 7, $6, 100, $7);
label $1:
%2 = con(w(4));
br($2);
label $2:
%3 = phi(w, %2, $1, %5, $7, %0, $6, %0, $5, %0, $4, %4, $3, %1, $0);
retn(%3);
label $3:
%4 = call w(@foo, in w %0);
br($2);
label $4:
br($2);
label $5:
br($2);
label $6:
br($2);
label $7:
%5 = con(w(3));
br($2);
};
This is what clang/LLVM gives us
Our clang/LLVM is almost unchanged
Backends for other architectures get this too
(edited for clarity)

## Slide 29
The genAsm
(edited for clarity)
These are Mill operations
and their arguments
define external function @bar w (in w) {
label $0:
%1 = con(w(1));
switch(%0, $1, 0, $2, 2, $3, 3, $3, 5, $4, 6, $5, 7, $6, 100, $7);
label $1:
%2 = con(w(4));
br($2);
label $2:
%3 = phi(w, %2, $1, %5, $7, %0, $6, %0, $5, %0, $4, %4, $3, %1, $0);
retn(%3);
label $3:
%4 = call w(@foo, in w %0);
br($2);
label $4:
br($2);
label $5:
br($2);
label $6:
br($2);
label $7:
%5 = con(w(3));
br($2);
};

## Slide 30
The genAsm
define external function @bar w (in w) {
label $0:
%1 = con(w(1));
switch(%0, $1, 0, $2, 2, $3, 3, $3, 5, $4, 6, $5, 7, $6, 100, $7);
label $1:
%2 = con(w(4));
br($2);
label $2:
%3 = phi(w, %2, $1, %5, $7, %0, $6, %0, $5, %0, $4, %4, $3, %1, $0);
retn(%3);
label $3:
%4 = call w(@foo, in w %0);
br($2);
label $4:
br($2);
label $5:
br($2);
label $6:
br($2);
label $7:
%5 = con(w(3));
br($2);
};
(edited for clarity)
These are basic blocks
and their uses

## Slide 31
The genAsm
define external function @bar w (in w) {
label $0:
%1 = con(w(1));
switch(%0, $1, 0, $2, 2, $3, 3, $3, 5, $4, 6, $5, 7, $6, 100, $7);
label $1:
%2 = con(w(4));
br($2);
label $2:
%3 = phi(w, %2, $1, %5, $7, %0, $6, %0, $5, %0, $4, %4, $3, %1, $0);
retn(%3);
label $3:
%4 = call w(@foo, in w %0);
br($2);
label $4:
br($2);
label $5:
br($2);
label $6:
br($2);
label $7:
%5 = con(w(3));
br($2);
};
(edited for clarity)
These are Static Single Assignment operands
and their uses

## Slide 32
The genAsm
define external function @bar w (in w) {
label $0:
%1 = con(w(1));
switch(%0, $1, 0, $2, 2, $3, 3, $3, 5, $4, 6, $5, 7, $6, 100, $7);
label $1:
%2 = con(w(4));
br($2);
label $2:
%3 = phi(w, %2, $1, %5, $7, %0, $6, %0, $5, %0, $4, %4, $3, %1, $0);
retn(%3);
label $3:
%4 = call w(@foo, in w %0);
br($2);
label $4:
br($2);
label $5:
br($2);
label $6:
br($2);
label $7:
%5 = con(w(3));
br($2);
};
(edited for clarity)
This is our switch
, the selector
, the cases,
and the targets

## Slide 33
shift
mul
Wide issue
The Mill is wide-issue, like a VLIW or EPIC
mul
shift
add
PC
slot #
0
1
2
instruction
Instruction slots correspond to function pipelines
mult’er
shifter
adder
mult’er
shifter
adder
mult’er
shifter
adder
pipe #
0
1
2
Decode routes ops to matching pipes
add

## Slide 34
The conAsm
This is the first instruction of function “bar”:
(edited for clarity)
Minor note: Mill is rather CISC, so things like function call and return are single ops, not lengthy multi-op idioms. Consequently they can be predicated instead of branched around: retntr (return if true)
function entry
function argument (“x”)
operations
Result operands
end of instruction
F("bar") %0;
rd(w(1ul)) %1,
rd(w(4ul)) %2,
eql(%0, 0) %7,
lsss(%0, 2) %8,
eql(%0, 4) %9,
retntr(%7, %1),
retntr(%8, %2),
retntr(%9, %2);

## Slide 35
The conAsm
F("bar") %0;
rd(w(1ul)) %1,
rd(w(4ul)) %2,
eql(%0, 0) %7,
lsss(%0, 2) %8,
eql(%0, 4) %9,
retntr(%7, %1),
retntr(%8, %2),
retntr(%9, %2);
This is the first instruction of function “bar”:
(edited for clarity)
drop constant 1, call it %1
drop constant 4, call it %2
drop bool “x==0”, call it %7
drop bool “x<2”, call it %8
drop bool “x==4”, call it %9
if %7 (x==0) return %1 (1)
if %8 (x<2), return %2 (4)
if %9 (x==4), return %2 (4)
But… retntr(%7, %1) uses results produced in the same instruction!
How?

## Slide 36
Phasing
rd(w(1ul)) %1,
rd(w(4ul)) %2,
How can an op use the result of another op in the same instruction?
eql(%0, 0) %7,
lsss(%0, 2) %8,
eql(%0, 4) %9,
retntr(%7, %1),
retntr(%8, %2),
retntr(%9, %2);
A Mill instruction is not a collection of ops that issue together
It is a collection of three-operation dataflows
that are phase-issued over three cycles.
Dataflows of consecutive instructions partially overlap
cycle boundary

## Slide 37
The whole thing
F("bar") %0;
rd(w(1ul)) %1,
rd(w(4ul)) %2,
eql(%0, 0) %7,
lsss(%0, 2) %8,
eql(%0, 4) %9,
retntr(%7, %1),
retntr(%8, %2),
retntr(%9, %2);
rd(w(3ul)) %5,
con(w(100ul)) %15,
rd(w(4ul)) %16,
rd(w(4ul)) %17,
lsss(%0, 8) %13,
eql(%0, %15) %14,
calltr1(%13, "foo", %0) %4,
pick(%14, %5, %2) %18,
retntr(%13, %4),
retn(%18);
eql(%0, 5) %10,
eql(%0, 6) %11,
eql(%0, 7) %12,
retntr(%10, %0),
retntr(%11, %0),
retntr(%12, %0);
Yes, that’s the whole function
Three instructions
Three cycles max
Fewer if early-out
ILP == 8

## Slide 38
The whole thing
F("bar") %0;
rd(w(1ul)) %1,
rd(w(4ul)) %2,
eql(%0, 0) %7,
lsss(%0, 2) %8,
eql(%0, 4) %9,
retntr(%7, %1),
retntr(%8, %2),
retntr(%9, %2);
rd(w(3ul)) %5,
con(w(100ul)) %15,
rd(w(4ul)) %16,
rd(w(4ul)) %17,
lsss(%0, 8) %13,
eql(%0, %15) %14,
calltr1(%13, "foo", %0) %4,
pick(%14, %5, %2) %18,
retntr(%13, %4),
retn(%18);
eql(%0, 5) %10,
eql(%0, 6) %11,
eql(%0, 7) %12,
retntr(%10, %0),
retntr(%11, %0),
retntr(%12, %0);

## Slide 39
Phasing
How can an op use the result of another op in the same instruction?
cycle boundary
rd(w(1ul)) %1,
rd(w(4ul)) %2,
eql(%0, 0) %7,
lsss(%0, 2) %8,
eql(%0, 4) %9,
retntr(%7, %1),
retntr(%8, %2),
retntr(%9, %2);
lsss(%0, 8) %13,
eql(%0, %15) %14,
calltr1(%13,
"foo", %0) %4,
retntr(%10, %0),
retntr(%11, %0),
retntr(%12, %0);
eql(%0, 5) %10,
eql(%0, 6) %11,
eql(%0, 7) %12,
rd(w(3ul)) %5,
con(w(100ul)) %15,
rd(w(4ul)) %16,
rd(w(4ul)) %17,
retntr(%13, %4),
retn(%18);
But wait – that’s five cycles, not three!
No it’s not:
the end cycles overlap with the caller
in caller
in caller
in bar()
(unused)
Same overall dataflow schedule as OOO

## Slide 40
But – what about mispredicts?
F("bar") %0;
rd(w(1ul)) %1,
rd(w(4ul)) %2,
eql(%0, 0) %7,
lsss(%0, 2) %8,
eql(%0, 4) %9,
retntr(%7, %1),
retntr(%8, %2),
retntr(%9, %2);
rd(w(3ul)) %5,
con(w(100ul)) %15,
rd(w(4ul)) %16,
rd(w(4ul)) %17,
lsss(%0, 8) %13,
eql(%0, b0 %15) %14,
calltr1(%13, "foo", %0) %4,
pick(%14, %5, %2) %18,
retntr(%13, %4),
retn(%18);
eql(%0, 5) %10,
eql(%0, 6) %11,
eql(%0, 7) %12,
retntr(%10, %0),
retntr(%11, %0),
retntr(%12, %0);
This code is really the chain-of-ifs, using retntr instead
Seven retntr == 7 chances to miss?
NO!
One prediction to rule them all

## Slide 41
Extended Basic Blocks (EBBs)
EBB
branch
EBB
Program
counter
EBB
EBB
EBB chain
The Mill groups code into Extended Basic Blocks, single-entry multiple-exit sequences of instructions.
Branches can only target EBB entry points; it is not possible to jump into the middle of an EBB.
Execution flows through a chain of EBBs

## Slide 42
Predicting EBBs
EBB
branch
With an EBB organization, you don’t have to predict each branch. Only one of possibly many branches will pass control out of the EBB – so predict which one.
If control enters here -
predict that control will exit here
The Mill predicts exits, not branches.

## Slide 43
With branch prediction
x == 5
x == 6
x == 3
x == 0
x == 2
x == 7
x == 100
actual
All predicted-taken branches before the branch to the selected target will miss.
The selected target will miss too if it was predicted not-taken.
F
F
T
F
T
F
T

## Slide 44
With exit prediction – early miss
x == 5
x == 6
x == 3
x == 0
x == 2
x == 7
x == 100
predicted
actual
Early miss:
  miss occurs before predicted
One miss penalty, same as branch prediction early miss

## Slide 45
With exit prediction – late miss
x == 5
x == 6
x == 3
x == 0
x == 2
x == 7
x == 100
predicted
actual
Late miss:
  miss occurs after predicted
One miss penalty at predicted, one at actual, vs. potentially one at every branch
But – a uniform case distribution means no prediction is made, will run out ebb for one miss total

## Slide 46
Brag
Research shows 88% of OOO advantage is due to better static schedules; only 12% is due to dynamic schedules such as overlapping memory misses.
Discerning the Dominant Out-of-Order Performance Advantage: Is it Speculation or Dynamism? – McFarlin et al., ASPLOS ‘13
Immunity to anti- and output hazards, fault-transparent speculation, and phasing gives Mill the 88%. We get the 12% in other ways. Those schedules can sustain the full width of the machine, not limited to 4 issues/cycle sustained.
In other words, a 17-wide Out-of-Order machine can probably keep up with a mid-range Mill.
Until it melts.

## Slide 47
Want more?
Sign up for technical announcements (no marketing):
MillComputing.com/#Newsletter
Videos of other talks, manuals, papers:
MillComputing.com/docs
Want to work on the Mill?
MillComputing.com/#JoinUs

## Slide 48
AMA
Ask me anything!

## Slide 49
Postscript
Maybe you thought doing the whole example in three instructions was pretty good?
So did we.
Then Forum reader @Veedrac wrote it in two
F('bar') %0;
con (w(100ul)) %1,
rd (w(1ul)) %2,
rd (w(3ul)) %3,
rd (w(4ul)) %4,
eql (%0, %1) %5,
gtrs (%0, 7) %6,
gtrs (%0, 3) %7,
eql (%0, 0) %8,
pick (%8, %2, %4) %9,
retntr (%5, %3),
retntr (%6, %4),
retntr (%7, %0);
gtrs (%0, 1) %10,
calltr1(%10, 'foo', %0) %11,
retnfl (%10, %9),
retn (%11);
A compiler writer’s job is never done
Sigh! 

## Slide 50
Want more?
Sign up for technical announcements (no marketing):
MillComputing.com/#Newsletter
Videos of other talks, manuals, papers:
MillComputing.com/docs
Want to work on the Mill?
MillComputing.com/#JoinUs