## Slide 1
Number thirteen of a series
Drinking from the Firehose
Threading in the Mill
CPU Family

## Slide 2
Encoding
The Belt
Memory
Prediction
Metadata and speculation
Execution
Security and reliability
Specification
Software pipelines
The compiler
Switches
Inter-process communication
Threading
Wide Data
Benchmarks
Slides and videos of other talks are at:
millcomputing.com/docs
You are here
Talks in this series

## Slide 3
The Mill CPU
The Mill is a new general-purpose commercial CPU family.
The Mill has a 10x single-thread power/performance gain over conventional out-of-order superscalar architectures, yet runs the same programs, without rewrite.
This talk will explain:
  Mill hardware thread creation and dispatch
  Threading interaction with protection and security
  Cooperation and preemption
  And will touch on exception handling too

## Slide 4
The Mill ISA
Mill is wide-issue – 30+ MIMD ops per cycle
Mill is statically scheduled – no issue hazards or OOO
Mill is exposed pipeline – all ops have fixed latency
Mill has integrated vectors – all scalar ops are vector too
Mill has hardware SSA – no general registers

## Slide 5
What about the OS?
The operating system is an application
- like any other.
There are no privileged operations.
There is no Supervisor Mode.
All protection is by byte address range.

## Slide 6
Caution!
Gross over-simplification!
This talk tries to convey an intuitive understanding to the non-specialist.
The reality is more complicated.
(we try not to over-simplify, but sometimes…)

## Slide 7
Mechanism vs. policy
This talk is about mechanism – how Mill threading works.
It’s not about policy – how the mechanism is used.
The Mill is a general-purpose CPU architecture.
It’s not a Unix machine.
It’s not a Windows, …, machine.
It’s not a C machine.
It’s not a Java, …, machine.
It’s a platform in which each of those can implement their own threading model.
To the extent that they have one.

## Slide 8
Some philosophy
Threading must be unobtrusive, understandable, and cheap
or it won’t be used.

## Slide 9: The normal thread stack
The data stack is list of frames
Every time you call a function you get a new frame
Frames need link pointers to track which function to return to
Stack Overflow!
Return Oriented Programming!

## Slide 10: The Mill secure thread stack
The data stack is list of frames
Every time you call a function the function gets a new frame
Frames need link pointers to track which function to return to
The Mill spiller manages a secure call stack
Inaccessible to programs
And stack access is range-checked
fault

## Slide 11
Interrupts, traps and faults
These are just involuntary calls
Hardware vectors to the entry point
Hardware supplies the arguments
No duplicated state
No task switch
No pipeline flush
No restart penalty after return
A mispredict (4 cycles + cache) is the only delay

## Slide 12: Processes
A Unix process has:
  An id
  Some resources
  Some permissions
  At least one thread
a process
72
TLB
threads

## Slide 13: Processes
But – a process is a software concept – and the Mill is hardware
So the concept is split into the hardware parts
a process
72
TLB
threads
hardware permissions
hardware threads
left for software

## Slide 14: Turfs
All Mill protection is by memory permissions
The turf is the Mill ”protection domain”
A turf holds permissions for a collection of memory regions
Turfs give cheap secure memory isolation
Turf != process:
  Turfs don’t have to have associated threads
  Threads are not bound to a turf

## Slide 15
Turfs
turf 5
A thread runs in a turf – one turf at a time, but can change to a different turf via a portal call.
whole address space
region descriptors

## Slide 16
Turfs
turf 17
turf 5
Note that the descriptors of a turf can describe overlapping regions, possibly with different rights.
And that the descriptors of two different turfs can describe the same region, possibly with different rights.
A different turf conveys rights to other regions.

## Slide 17
Turfs
turf 17
turf 5
A thread runs in a turf – one turf at a time, but can change.
While running in turf 5
While running in turf 17
A thread can see and use
A register holds the current turf ID for the thread.
Many threads can be in the same turf concurrently.

## Slide 18
Turfs
regions
region desc:
LWB
UPB
rights
turf ID
address space
A thread also has a unique non-forgeable global id.
At power-up, hardware starts an initial thread in the
All turf, the whole 60-bit address space with all rights.
Your vision increases as you approach the All.
Swami Suchananda
Region descriptor turf ids may be wild-carded.

## Slide 19: Portals
Like a function call, but changes turf too
You can call between many turfs in any order
You can re-enter a turf
secure stack
data stack

## Slide 20: Portal calls
void handle_request(packet* pkt) {
decrypt(pkt->buf, pkt->buflen);
...
request is turf 17
void decrypt(void* buf, size_t len) {
...
return;
}
thread 9
private key is turf 20
httpd
request
private key
decrypt(buf)
request
private key
turf 17
turf 20

## Slide 21: Threads and Turfs
A portal call lets you switch turf quickly
Dispatch lets you switch thread quickly
turfs
threads

## Slide 22: Dispatch
Each core is running an active thread
Other threads are parked
The dispatch op activates a parked thread -
and parks the thread you were in
This is not a priviledged op – any thread/turf can dispatch
A spawn starts threads and dispatch resumes them
A thread can only be active on one core at a time

## Slide 23: Dispatching
It doesn’t matter if a thread has already portaled through several turfs
It matters which turf the thread is currently in
Active dispatcher and parked dispatchee must be in the same turf
Turf 3
Turf 9
Turf 6
Turf 9
Turf 34
Thread 3 active in turf 9
Thread 12 parked turf 9
Thread 3 parked in turf 9
Thread 12 active turf 9
Turf 9
Turf 9
dispatch

## Slide 24: Mill Chess
19
17
18
20
16
4
5
6
7
8
9
9
10
11
12
13
14
A portal call lets you switch turf very quickly
And the dispatch op lets you switch thread very quickly
No knight moves!
17
20
thread 12
turfs
thread 9

## Slide 25: Concurrency vs Parallelism
Concurrency is when tasks can start, run, and complete in overlapping time periods
Parallelism is when more than one task is running at the exact same instant
one core = concurrency
two cores = parallelism

## Slide 26: Cooperative multi-threading
For example, a goroutine is started to fetch a url
The RTS spawns a new thread
And dispatches to it
This immediately stalls waiting on IO,
so the RTS dispatches to another runnable goroutine
Which spawns another goroutine to fetch a url...
func fetch(u) {
r, e =
http.Get(u)
...
thread 42
thread 11
thread 1032
for u in urls {
go fetch(u)
}
...
func fetch(u) {
r, e =
http.Get(u)
...
for u in urls {
go fetch(u)
}
...
func fetch(u) {
r, e =
http.Get(u)
...

## Slide 27: Dispatching cooperatively
A lot like fast stack switching for ”lightweight threads” and goroutines etc
Except that it’s secure
And its not a problem to call syscall portals into the kernel or other services
Cooperative multi-tasking is concurrency not parallelism

## Slide 28: Preemptive multi-threading
The kernel sets a hardware timer
When the timer fires, the kernel handles the interrupt
in the kernel turf
Kernel has a ‘run queue’
And decides who to dispatch to next...
func fetch(u) {
r, e =
http.Get(u)
...
thread 42
thread 11
thread 1032
for u in urls {
go fetch(u)
}
...
func fetch(u) {
r, e =
http.Get(u)
...
for u in urls {
go fetch(u)
}
...
program turf
func fetch(u) {
r, e =
http.Get(u)
...
void timer() {
next =
ready.pop();
dispatch(next);
Kernel turf
void timer() {
next =
ready.pop();
dispatch(next);

## Slide 29: Blocking IO
func fetch(u) {
r, e =
http.Get(u)
...
A thread calls a syscall portal to perform some blocking IO
If the buffer is empty, the kernel will find another thread to run from its ‘run queue’
Leaving the thread parked in the kernel turf ready to be resumed later when the buffer is no longer empty
thread 42
thread 11
thread 1032
for u in urls {
go fetch(u)
}
...
func fetch(u) {
r, e =
http.Get(u)
...
for u in urls {
go fetch(u)
}
...
program turf
void rd(f, b) {
...
Kernel turf
void rd(f, b) {
...
func fetch(u) {
r, e =
http.Get(u)
r.read(buf)
func fetch(u) {
r, e =
http.Get(u)
read(r, buf)

## Slide 30: Preemption
Kernel Turf
The kernel sets a hardware timer
When the timer fires, the core looks in the trap and fault handler array for the current turf
Trap and fault handlers can be portals -
so the interrupt is serviced in a kernel turf
Turf 3
Turf 9
Thread 6 active
trap

## Slide 31: Preemption
Turf 9
Kernel Turf
Kernel has a ’ready queue’
And decides who to dispatch to next...
And dispatches…
Turf 3
Thread 6 active
Kernel Turf
Turf 42
Thread 4 parked

## Slide 32: Preemption
Turf 9
Kernel Turf
Kernel has a ’ready queue’
And decides who to dispatch to next...
And dispatches…
Turf 3
Thread 6 parked
Kernel Turf
Turf 42
Thread 4 active

## Slide 33: Preemption
The kernel puts the parked thread into the ready queue.
Resets the timer.
And returns back to the application.
Turf 9
Kernel Turf
Turf 3
Thread 6 parked
Kernel Turf
Turf 42
Thread 4 active

## Slide 34: Spillets
The spiller stores the secure stack in a spillet.
Each spiller frame contains the saved belt and instruction pointers to restore to on function return.
When a spillet is full, an overflow spillet is allocated by the OS from a heap.
There is one spillet per thread, at a calculated address.
a spillet
an overflow spillet
...
Notes: Many more spiller frames than shown

## Slide 35
Stacklets
A thread in a service needs its own stack.
stack
application
service A
service B
The logical stack of each thread is a chain of stacklets, one for each turf entered by a nested portal call.
portal call
portal call

## Slide 36
stacklets
There is one stacklet per thread per turf.
frame
application
service
frame
WKR
application portal-calls service
WKR
WKR register limits access to only the live part of stack

## Slide 37
stacklets
There is one stacklet per thread per turf.
frame
application
frame
service
frame
WKR
service back-calls application
WKR

## Slide 38
stacklets
There is one stacklet per thread per turf.
frame
application
frame
service
frame
WKR
application re-calls service (nested)
WKR
frame
All frames of a turf/thread combination are adjacent in the stacklet; only one stack-WKR needed.
But – how can you allocate a stacklet in the middle of a portal call?

## Slide 39
Stacklet allocation
Stacklets are allocated in the address space, but not in DRAM.
One sixteenth of the address space is reserved for stacklets.
stacklets
stacklets are laid out as a two-dimensional array indexed by turf and thread ID.
thread
14
15
17
16
19
18
turf
34
35
36
37
{thread 17 in turf 36}

## Slide 40
thread ID
turf ID
0
63 59 55 33 11 0
0xf
stacklet allocation
A portal can compute a stacklet address without allocation
stack
portal call to turf 9
4KB
thread 17 in turf 5
0xf00004400005000
stacklet address
0xf00004400009000
A portal call uses address space.
The space is implicitly zero.
http://millcomputing.com/docs/memory

## Slide 41
What about callbacks?
If every portal call started a new stack at the thread/turf address, then a callback would put its stack on top of the previous stack:
portal call to turf 9
thread 17 in turf 5
portal call back to turf 5
Oops!

## Slide 42
The stacklet info block
Associated with each stacklet, and also at a computed address, is a cache-line sized info block with metadata.
TOS
base
limit
The values are offsets from the computed stacklet address, biased so that all are zero for an unused stacklet.
A portal call writes the current stack range to the info block
and fetches the new info block to update the stack WKR.
Because “empty” is all zero, and unbacked loads are implicitly zero, an unused stacklet is empty.
A portal call costs two fetches: the portal and the info block.

## Slide 43: Thread creation
19
17
18
20
16
4
5
6
7
8
9
9
10
11
12
13
14
thread 15
17
thread 9
The spawn op creates a new hardware thread
This is not a priviledged op – any turf can spawn
The new thread is initially parked in your turf
You specify the entry point and initial belt
Hardware thread ids are given out in random order
When the thread is resumed it’s as though called with the belt you supplied

## Slide 44: Stack fragments
The hardware manages the call stack securely
Consecutative frames in the same turf are known collectively as a fragment
data stack fragments
call stack fragments
spillet
stacklet chain

## Slide 45: Exceptional unwind
Exceptional unwind – C++ -style exceptions and longjmps etc. – is managed by hardware too
If an exception is uncaught when unwinding to another fragment,
Then the hardware flags the turf’s next fragment to propagate the exception
And the portal caller gets a trap they can handle
data stack fragments
call stack fragments
bye
trap
spillet
stacklet chain

## Slide 46: HEYU
HEYU
Exceptions – interrupts, signals – can be induced in other threads in the same turf using the HEYU op
The topmost frame belonging to the turf is flagged
And will trap immediately if actually running
Else will trap as soon as it’s unwound to
trap
spillet
stacklet chain
Notes: HEYU is homage to the Borroughs

## Slide 47: Thread death
A thread may have entered many turfs
A thread can even enter the same turf more than once
A turf doesn’t own a thread; it shares it with all other turfs on the call stack
But a thread in a turf can die using the suicide op or faulting
Its stacklets are invalidated
Turf 12
Turf 3
Turf 12
Turf 12
Turf 12
bye
spillet
stacklet chain

## Slide 48: Thread death
Its data stacks can be reclaimed
As the call stack unwinds, invalid spiller frames can be discarded
As the unwind reaches live frames the error is reported for the turf to handle gracefully
Eventually the stacklet is empty and is discarded too
Turf 12
Turf 3
Turf 12
Turf 12
Turf 12
bye
spillet
stacklet chain

## Slide 49
Shameless plug
For technical info about the Mill CPU architecture:
http://millcomputing.com/docs
To sign up for future announcements, white papers etc.
http://millcomputing.com/mailing-list